## Slide 1: Way forward for FR2 fallbacks
Ericsson, Apple, US Cellular, T-Mobile US, Verizon, Bell Mobility, AT&T, Turkcell, SK Telecom, Softbank, LG Uplus, Telstra, Reliance Jio, Telecom Italia, British Telecom, Orange, Deutsche Telekom, CHTTL
RP-201538
RAN#89-e Online
2020-09-14 – 2020-09-18

## Slide 2: Background
At RAN#88 a compromise was discussed for the FR2 fallback topic which had two parts:
  1. UE must support all the fallback band combinations
  2. UE conformance requirements w.r.t. the fallback band combinations are relaxed
The details of bullet 2 was open and hence the topic was postponed to RAN#89.

## Slide 3: Proposed way forward
It is proposed that:
  UE must support all the fallback band combinations
  UE conformance requirements w.r.t. the fallback band combinations are relaxed:
    The fallback band combinations fulfilling both the following conditions are exempt from requirements:
      consists of multiple sub-blocks
      has at least one sub-block comprising a contiguous CA combination (i.e. a letter B, C, D, …).
  The UE shall comply to all regulatory requirements for all supported band combinations, i.e. including for all fallback band combinations.

## Slide 4: Detailed wording for 38.101-2 and 38.101-3
For FR2 intra-band CA combinations with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination, there are no RF performance requirements for the fallbacks with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination. Requirements in other specifications are not affected. NOTE: The above is an exception with regards to compliance to RF performance requirements. The exception applies to fallback band combinations consisting of multiple subblocks where at least one of the subblocks consists of a contiguous CA combination. The exception does not apply to other band combinations.
CRs are found in that the sourcing companies proposes to approve:
RP-201872, RP-201873, RP-201874, RP-201875