## Slide 1: FR1-FR2 BCS ambiguity in 38.101-3
Ambiguity prevents product implementation and bears risk of configuration failures.
TSG RAN#91e
RP-210665
source: Ericsson

## Slide 2: Observed Ambiguity in 38.101-3
Question: Which Bandwidth Combination Sets (BCS) apply for FR1-FR2 Dual Connectivity?
Interpretation A: BCSs for FR1+FR2 DC are inherited from FR1 CA tables in 38.101-1 and from FR2 CA tables in 38.101-2
  Inline with text in tables in section 5.5B.7: "NOTE 1: NR configuration for FR1 and FR2 are defined in TS 38.101-1 [2] and TS 38.101-2 [3] respectively."
  Unclear how to lookup two BCS rows in two specs with a single supportedBandwidthCombinationSet ID in ASN.1.
  BCS-lookup and definitions would be different for FR1-FR2 DC and CA (unless BCSs in 101-3 are removed for CA)
  Required changes:
    Change so that supportedBandwidthCombinationSet ID is used for BCS-lookup in 38.101-1 (FR1)
    If RAN4 introduces as BCS>0 in 38.101-2, RAN2 needs to add a supportedBandwidthCombinationSet-FR2 to ASN.1
    For FR1+FR2 CA, remove BCS definitions in tables in 38.101-3 and refer instead to BCS definitions in 38.101-1 and 38.101-2
Interpretation B: BCSs for FR1+FR2 DC are inherited from FR1+FR2 CA tables in 38.101-3 (section 5.5A.1)
  Similar to BCS lookup for FR1+FR1 DC in FR1 CA tables (see 38.101-1): "For an NR DC configuration specified in 5.5B.1-1, the bandwidth combination sets for the corresponding NR CA configuration in 5.5A.3 {...} are applicable""
  The existing supportedBandwidthCombinationSet signaled in ASN.1 is sufficient for the lookup.
  Required change: Change 38.101-3 so that FR1+FR2 CA tables in 38.101-3 are used for BCS lookup

## Slide 3: Proposals
Proposal 1: Resolve the BCS ambiguity in 38.101-3 to allow for timely product implementation and to avoid compatibility issues with early UEs on the market.
Proposal 2: BCSs for FR1+FR2 DC are inherited from FR1+FR2 CA tables in 38.101-3 (section 5.5A.1)
Proposal 3: Approve the corresponding CR (Interpretation B)
Company CRs for 38.101-3 are in RP-210666 (Interpretation A) and RP-210667 (Interpretation B)