## Slide 1: Considerations on Rel-17 Positioning Architecture
Ericsson, FirstNet, AT&T
3GPP TSG RAN#96
Budapest, Hungary, 6-9 June 2022
Agenda Item: 9.7.1.5
RP-221631

## Slide 2: Issues with PRU discussion handling in Rel-17 (1)
Discussion first brought by RAN1 in LS R1-2106326
  "The term “positioning reference unit (PRU)” is only used as a terminology in this discussion. PRU does not necessarily mean an introduction of a new network node.“
Other WGs replies:
  SA2 :
    S2-2109105: "SA2 discussed the PRU and agreed to include the objective of how to support the PRU in Rel-18 eLCS_Ph3 Study Item, considering SA2 Rel-17 is already frozen and more time is needed to study how to support the PRU in SA2. […] SA2 does not have enough time in Rel-17 to comment on such solutions at the present time but expects that a solution or solutions preferable to SA2 should be possible in Release 18."
    S2-2109104: "SA2 has finished R17 work on 5G_eLCS_Ph2, therefore it is not possible to study this topic in this release. SA2 may study support of PRUs in Release 18 in which case a better solution may be available later."
  RAN2:
    R2-2203597: "RAN2 has agreed that RAN2 will not discuss PRUs further without further guidance from RAN1 (LS or feature list)."
  RAN3:
    R3-214457: “[…] if the PRU functionality were to be part of the gNB (from LMF perspective) e.g., realized as a TRP, then RAN3 specification impacts (if any) would require further scoping and evaluation.“
RAN1 final agreement: “from RAN1 perspective, no change to RAN1 specifications is needed in order to support PRU in Rel-17”
Observation 1: The discussion should not have started from RAN1, as network architecture is not part of RAN1’s ToR

## Slide 3: Issues with PRU discussion handling in Rel-17 (2)
A PRU cannot replace a gNB (it is a UE)
Further discussion happened at RAN2 #118-e
  (RAN2 is indeed the right group to discuss positioning architecture, together with RAN3)
  “How to handle PRU”: [R2-2206386, Report of [AT118-e][622][POS] 38305 positioning CR, Intel (moderator)]
    10 comments received
      6 in favor of keeping the stage 2 description of the PRU
      3 comments pointing out that without further details the current description does not help much in implementing the PRU; proposals were made for further clarification or to move it to an info annex
      1 in favor of removing the stage 2 description of the PRU
  Stage 2 for positioning was never discussed online, as stage 3 was prioritized
    It was claimed, “Stage 2 can be fixed later”
  PRU description is currently captured in TS 38.305
Observation 2: It is hard to claim that there was real “consensus” in RAN2 to keep the PRU description in TS 38.305 Rel-17

## Slide 4: Proposal
Proposal: Given the above history of discussions, discuss whether it is appropriate to have the PRU captured in TS 38.305 Rel-17; if agreeable, consider whether to move it to an info annex or remove it