## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Young Ik Jo
Status Report for RAN WG3
3GPP TSG RAN #97, Electronic Meeting
Sep 12th – 16th, 2022
RP-221890

## Slide 2: Executive Summary
Total 744 Tdocs at submission deadline (excluding LSin received from other groups) in Q3
  5% LSs and related documents
  38% Maintenance: Rel-17 & earlier
  58% Documents to Rel-18 WIs/SIs
Updated endorsed guidelines for e-meeting: R3-224230
The R18 NR Network-Controlled Repeaters SI (led by RAN1) and the R18 Enhancement for Resiliency of gNB-CU-CP SI(led by RAN3) are completed in RAN3.
RAN3#117-e | Aug 15th – 24th, 2022
RAN #97e | Sep 12th – 16th, 2022

## Slide 3: Tdoc submitted to RAN3
The total number of contributions around 900 for each RAN3 meeting is affordable
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: Overview of RAN3-led Rel-18 NR SI/WIs
 | Name (acronym) | Acronym | Rel | Leading WG | other impacted WGs | Old % (the same as in WI/SI SR) | New % | Target completion | Remark/updates/SR
941009 | Mobile IAB (Integrated Access and Backhaul) for NR WI | NR_mobile_IAB | R18 | R3 | R2 | 0% | 5% | 12/23 | WID: RP-221815 SR: RP-222159
941008 | Enhancement on NR QoE management and optimizations for diverse services WI | NR_QoE_enh | R18 | R3 | R2 | 0% | 10% | 12/23 | WID: RP-221803 SR: RP-222219
941010 | Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN WI | NR_AIML_NGRAN | R18 | R3 | R2 | 0% | 10% | 06/23 | WID: RP-220635 SR: RP-222123
941007 | Further enhancement of data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) WI | NR_ENDC_SON_MDT_enh2 | R18 | R3 | R2 | 0% | 10% | 12/23 | WID: RP-221825 SR: RP-222122
940088 | Enhancement for resiliency of gNB-CU-CP SI | FS_gNB_CU_CP_resiliency | R18 | R3 |  | 0% | 100% | 09/22 | SID: RP-221438 SR: RP-222250
WI: Black SI: Blue Completed WI/SI: Red

## Slide 6: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-221891, which includes:
  108 CRs were agreed at the RAN3#117-e meeting.
  2 Rel-15 Cat.F CRs
  13 Rel-16 CRs: 2 Cat.A CRs, 11 Cat.F CRs
  93 Rel-17 CRs: 10 Cat.A CRs, 5 Cat.B CRs, 78 Cat.F CRs
    Cat.F in R3-225228 Support for flexible gNB ID length [gNB_ID_Length] (stage2 endorsed)
    3 Cat.F in R3-225070 (stage2 endorsed), R3-224340, R3-224339 Timer handling for CHO with SCG configuration [CHOwithDCkept]
    Cat.B in R3-225274 Correction of LTE MDT on Sensor information[LTE-Height-MDT]
    Split R3-224920 to two companies CRs in order to link to the TEI CRs agreed in RAN2:Cat.B in RP-222168 Correction of LTE MDT on event trigger logging [LTE-Event-MDT] and Cat.B in RP-222172 Correction of LTE MDT on Sensor information[LTE-Height-MDT].
  8 Non-Backwards-Compatible (NBC) CRs for Rel-17
    R3-224273, R3-225191, R3-225152, R3-225208, R3-225162, R3-225056, R3-225185, R3-225102
    (Here is how 3GPP works with NBC changes)
  11 endorsed draftCRs to RAN2 specs.

## Slide 7: Statistics for GTW Usage
Overall, roughly 30 hours of GTW conference calls in Q3
Statistics shown below
  TEI/LS items were handled via online and email discussions (7 hour of GTW time used)
  And remaining 23 hours of GTW conference call time was used for Rel-18 items
  GTW conference call time was mainly used for R18 WI/SIs, especially for those SIs planned to be closed in one meeting, Resiliency of gNB-CU-CP SI and NCR SI, while for R17 TEIs, some controversial issues cost more online time compared with time planned, e.g., SON/MDT, positioning.

## Slide 8: R18 SON/MDT WI
Progress in the last quarter
Support of SON/MDT Enhancements：
- SHR for intra-system inter-RAT, HO from NR to LTE will be treated first,
- SPCR for NR-DC, including(SN- and MN-initiated classic PSCell change / CPC; Intra-SN classic PSCell change / CPC; Classic Addition / CPA; HO with SN change are not prohibited, but possibly addressed once the basic solution for SPCR is known)
- MRO for CPC and CPA based on the R17 NR-DC MRO solution.
- MRO for the fast MCG recovery(SCG fails or is deactivated when the UE attempts MCG recovery;The signalling delay is longer than the time the UE waits for the response,other problem are not precluded if legacy MRO mechanism cannot cope with it)
- RACH enhancements(RACH optimization for feature or feature combinations involving RACH partitioning ; RACH report retrieval,SN RACH report in MR-DC)
- SON/MDT enhancements for Non-Public Network(support of Signaling based MDT and Management based MDT for NPNs; Support both immediate MDT and logged MDT for NPN; User consent handling for NPNs, in particular SNPNs; Area scope for NPNs; Support of NPNs in RLF Report and other UE reports used for SON and MDT)

## Slide 9: R18 SON/MDT WI
Progress in the last quarter
NRU for MRO:
- Add to RLF report indications concerning Measured RSSI and HOF due to consistent LBT failure.
- Keep existing failure type definition and detection to indicate RLF or HOF or PSCell change failure due to consistent LBT failure.
- Add indications of consistent LBT failures in RA report.
NRU for MLB
- Exchange over Xn of Energy Detection Threshold for UL, and Channel Occupancy Time in UL is supported.
- Rename existing Energy Detection Threshold IE in F1AP and XnAP , and the details to be discussed in CB8.
MRO for inter-system handover for voice fallback
- Consider Case 1-2 for MRO enhancements for inter-system inter-RAT handover for voice fallback
MRO for MR-DC SCG failure
- Support MRO for SCG failure in EN-DC, NGEN-DC and NE-DC scenarios.
Other important info
Split the discussion based on the topics
Next steps
Continue to work on stage2 and stage3 for all features identified.

## Slide 10: R18 QoE WI
Progress in the last quarter
Support MBS broadcast service INACTIVE/IDLE QoE first.
UE handles area scope checking for QoE measurements in RRC_INACTIVE/IDLE mode.
UE shall keep QoE configuration for MBS broadcast service configured in RRC_CONNECTED even when UE switches to RRC_IDLE and RRC_INACTIVE.
If UE receives the MBS broadcast QoE configuration in RRC_CONNECTED state, Rel-17 QoE configuration mechanism is adopted as baseline.
In NR-DC senario, MN is responsible to configure the s-based QoE to UE. For M-based QoE configuration in NR-DC, coordination between MN and SN is needed. Details are FFS.
MN and SN should coordinate about configuring a dual-connected UE with RVQoE measurements.
QoE reports can be transmitted to either MN or SN and the reporting leg (MCG or SCG) can be changed during the application session.
Introduce the slice scope information in the configuration container, and send LS out to SA4.
UE should include QoS flow information in the RVQoE report to RAN. QoS flow information should be introduced as an explicit IE in the RAN visible QoE report over F1.
Next steps
Further discuss whether new mechanism for MBS broadcast QoE configuration shall be introduced
Further clarify the use case for high mobility scenario.
Continue to work on stage2 and stage3

## Slide 11: R18 AI RAN WI
Progress in the last quarter
Both non-split architecture and split architecture are in scope. Focus on the non-split architecture first. Split architecture should be specified after the work of non-split architecture. The training/inference function location is referred to TR37.817.
Capture the Abbreviations and general introduction of AI/ML in TS38.300.
Focus on Xn interface first. Start from SA and then consider DC.
Define a new procedure over Xn which can be used for AI/ML related information, e.g., predicted information.
The new procedure for reporting of AI/ML related information, e.g., predicted information, should be based in a requested way, like resource status report procedure.
RAN3 focus on the cell-level energy saving strategy as a start point, to avoid overlapped discussion for network energy saving SI.
Predicted resource status information of neighbouring NG-RAN node(s) generated by the current NG-RAN node is internally used, and no standard impacts.
The new procedure over Xn used for AI/ML related information should be non-UE associated as a start point.u
Predicted cell-granularity UE trajectory can be exchanged over Xn for AI/ML based mobility optimization.
Next steps
Continue to work on stage2 and stage3.

## Slide 12: R18 mobile IAB WI
Progress in the last quarter
As already supported in Rel17, a mobile IAB-MT and its co-located mobile IAB-DU may be served by different donor CUs. The mobile IAB donor that the co-located IAB-DU connects to may remain unchanged after the IAB-MT HO.
When IP connectivity between target IAB-donor DU and source IAB-donor CU is available, and when Xn connectivity between source and target donor CU is available, the Rel-17 partial migration is used as baseline for supporting the F1 transport migration and inter-donor routing when an mobile IAB-DU and its co-located mobile IAB-MT are connected to different donor CUs.
The mobile IAB-node may perform multiple consecutive partial migrations without inter-donor migration of its mobile IAB-DU.
For DU migration cases, to execute the handover of the served UEs, the mobile IAB-node concurrently supports two logical mobile IAB-DUs, which have F1AP associations with the source CU and the target CU, respectively.
The donor CU should know that the IAB node is “mobile”.
PCI space partitioning via OAM configuration can be used in some cases for avoidance of PCI collisions.
From RAN3 perspective, existing mechanism can be used for PCI collision detection in mobile IAB scenario.
Other important info
Enhancements/optimizations that are specific to the scenario where the mobile IAB-node connects to a stationary (intermediate) IAB-node or directly to a donor-DU are deprioritized.
RAN3 will not discuss separate authorization for mobile IAB without request by SA2.
Mobility of dual-connected mobile IAB nodes is down prioritized in Rel18.
No enhancements are needed for RACH collision avoidance unless requested by other WGs.
Next steps
Continue to work on stage2 and stage3
Notes: 刁雪莹

## Slide 13: R18 Mobility Enh. WI
Progress in the last quarter
For L1/L2 based inter-cell mobility, RAN3 focuses on the network-controlled procedure and will aim for a single solution for network signaling design support all agreed scenarios.
The gNB-CU initiates the L1/L2 mobility configuration procedure and initiates the configuration of candidate target cell(s) for L1/L2 mobility.
In Rel.18, RAN3 will continue the work on the CHO with SCG at the target. The scope will be limited to the data forwarding optimizations.
Regarding CHO with multiple SCGs at the target, RAN3 will wait for the progress in RAN2 before starting signalling design. At the next meeting, RAN3 will open discussion on the data forwarding aspects.
RAN3 considers SCG selective activation is prioritized in the Rel-18 work. It can be revisited based on RAN2 progress.
From RAN3 point of view, Rel-16/Rel-17 CPAC procedures are considered as start point for the Rel-18 work.
Other important info
More RAN2 input is expected and helpful.
Next steps
Continue to work on stage2 and stage3.

## Slide 14: R18 MBS WI
Progress in the last quarter
Part of factors identified for network to decide to enable UEs receiving multicast in RRC_INACTIVE state.
Guideline Identified for network sharing:
  NG-RAN shall be able to identify the MBS session signaling from different operators’ 5GCs aim at the same MBS session. The detail information is pending to SA2.
  Same PTM radio resource can be allocated in a shared cell for transmission of the same MBS service provided by different operators.
  The solution provided by RAN3 work on protocol in RAN sharing scenario should not have impact on Pre Rel-18 UE.
LS to RAN Plenary on the scope of the RAN WID.
Other important info
On multicast reception in RRC_INACTIVE, many key factors (e.g., loads on RACH, CM-CONNNECTED state UE context storage) should be evaluated in RAN2 first.
On multicast reception in RRC_INACTIVE, F1AP impacts depends on RAN2 solutions.
Next steps
Discuss the mobility support according to the progress in RAN2 and coordinate with RAN2.
Whether and which additional information (e.g., per MBS session level assistant information from 5GC, per-UE preference on multicast over RRC_INACTIVE) is needed by the gNB is FFS. (e.g., based on SA2 input)
Continue discussion on network sharing support (including identified scenarios).

## Slide 15: R18 Sidelink Relay WI
Progress in the last quarter
WA: NG-RAN receives the multi-path authorization from the AMF.
WA: Support U2U relay in CU-DU split architecture, FFS on the enhancements.
Reuse the existing network procedures to support single-hop L2 U2N Relay in Rel-18. Current signaling can support Scenario C, i.e., intra-gNB indirect to indirect path switch.
Source gNB decides to trigger path switching for the L2N remote UE.
From RAN3 perspective, multi-path scenario should be supported in Rel-18. Both intra-DU and inter-DU cases will be supported under the same gNB. Addition of direct/indirect path are supported.
The following use cases are not supported in Rel-18: Configure two indirect paths, More than two paths, Inter-gNB multi-path support.
Other important info
RAN3 waits for RAN2 progress on E2E PC5 QoS split for U2U relay.
RAN3 waits for the RAN2 progress on how to define control plane and user plane scenarios for multi-path support, and on whether and how to define the Primary path in multi-path support.
Next steps
RAN3 focuses on the XnAP and possible F1AP impacts to support the basic scenarios for service continuity.
RAN3 continues analyzing the selection of target Relay UE.
RAN3 will study the signaling impact on the direct or indirect path change under the same gNB for a UE connected via multi-path.

## Slide 16: R18 NR NTN WI
Progress in the last quarter
Mobility and Service Continuity Enhancements:
- In Rel-18, mobility enhancement based on NG and Xn can be discussed in WI based on technical issues to be solved.
- Enhancements for the support of CHO over NG for NTN-NTN hand-over should be discussed in this WI.
- The target gNB is able to uniquely identify the target cell based on the target cell information received from the source gNB.
- Time based CHO should be supported. Start time, duration are added in the signaling of time-based CHO.
- The exchange of NTN Cell Coverage Stop Time between gNBs may be further discussed in future RAN3 meetings.
Network verified UE location:
- The verification is performed in the CN.
- If the reported UE location is not correct, the CN will take necessary action and Rel-17 behavior can be kept as baseline. FFS on new cause value.
- RAN3 wait for RAN1/2 progress on the specific position method to be used for verification.
Next steps
Continue to work on stage2 and stage3.

## Slide 17: R18 IoT NTN WI
Progress in the last quarter
There is no need to provide the ephemeris info over S1.
Whether MME shall be aware of the coverage should be decided by SA2.
Paging enhancement for power saving should wait for the progress of RAN2 or SA2.
The mobility management enhancements for discontinuous coverage are pending RAN2 progress.
Next steps
Focus on the UE context release procedure due to discontinuous coverage and try to discuss the issue which SA2 has finalized, if any.

## Slide 18: R18 Resiliency of gNB-CU-CP SI
Progress in the last quarter
All the Failure Scenarios have been captured.
Keep companies' contributions in Annex.
Add following failure scenarios have been discussed:
- Hardware failure
- Software failure
- Transport network failure
- Power failure
- RAN node breakdown, e.g., due to natural disaster
Endorse R3-225251 as TR 38.879 v0.1.1.
Other important info
This SI is completed in RAN3.

## Slide 19: R18 NR NCR SI
Progress in the last quarter
pCR for NCR TR 38.867 has been agreed in R3-225252. The following aspects are captured:
  General procedures for 4 solutions on NCR management.
  Standard impacts analysis of all captured solutions.
  RAN3 SI conclusion.
LS to SA3, SA5 on questions for some captured solutions.
LS to RAN1 to inform RAN3 progress.
Other important info
The SI is completed from RAN3 perspective.
Next steps
Down selection of all captured solutions may take place in potential WI phase based on the feedback from other groups.

## Slide 20: R18 NR Positioning SI
Progress in the last quarter
From RAN3’s perspective, the current NG-RAN positioning architecture can in principle be re-used to support Sidelink Positioning in in-coverage and partial coverage scenarios.
Whether and how to support SL Positioning and Ranging Service Authorizations signalling to NG-RAN can be investigated by RAN3 during the WI phase, taking into account SA2 decisions on this aspect.
The potential impacts of SL resource pools, SL positioning measurements, UL CPP measurements, LPHAP, RedCap positioning and positioning Integrity on the RAN3 specifications can be examined during the WI phase, taking into account RAN1/RAN2 decisions.
Other important info
Potential RAN3 TU adjustment based on the progress of other WGs
Next steps
Pending on the progress from other WGs.

## Slide 21: R18 NR Network ES SI
Progress in the last quarter
Regarding the applicable scenarios for NES, RAN3 can consider both the overlaid scenario (i.e. heterogeneous scenario) and the non-overlaid scenario.
Regarding the load scenarios for NES, RAN3 can prioritise idle/empty and low/medium load scenarios, for which the SID has already described.
For those techniques determined by other groups, RAN3 can study the potential network interface impacts following the analysis/conclusions made in other groups. Note that parallel discussions are also possible due to the parallel meeting time.
RAN3 can study the network energy saving issues without involvement from other WG case by case.
LS on skeleton of TR 38.864 for NR network energy savings to RAN1 agreed in R3-225203.
Next steps
Identify the issues to be solved in RAN3 based on the progress in other WGs

## Slide 22: TEI Corrections
Progress in the last quarter
R17 SON/MDT corrections:
  Support UHI for CHO in Rel-17.Correction for TS 38.300/38.423/36.423 on UHI in MR-DC.
  For SON: Completion of the missing descripition of SCG MRO handling, Correction on Inter-system Resource Status Reporting, Correction on Report Caracteristics, Correction on NR-U for MLB.
  For MDT: Correction to early measurement collection,Correction on collection on beam measurement report configuration in M1.
R17 MBS corrections:
  Various LS addressed/noted; Missing stage 2 definition added; abnormal handling on NGAP addressed; MRB type indication on F1AP and per UE F1-U tunnel addressed; other miscellaneous corrections; corresponding CRs provided.
  Delay issue for the CU-CP to configure the multicastHFN-AndRefSN IE to the UE, wait for RAN2 progress. MBS session level data forwarding tunnel, E1AP impact on support of handover from non-supporting to supporting node, corrections to MC message flow in 38.401, exchanging of established broadcast service identity in neighbor cells on Xn to be continued.

## Slide 23: TEI Corrections
Progress in the last quarter
R17 Positioning Corrections:
  The signaling support for the timing error margin value reporting of UE/TRP TEG.
  Introduction of SRS port index and Measurement time occasion.
  Extending the legacy Measurement Periodicity by introducing a new IE for ECID.
  Addition of IE container for SRS-PosRRC-InactiveConfig-r17 into the POSITIONING INFORMATION RESPONSE message from DU to CU.
R17 Sidelink Relay
  The UE CONTEXT SETUP procedure of relay UE is not used to setup PC5 RLC channel for remote UE’s SRB1.
Gap related:
  Add NeedForGapNCSG-InfoNR, NeedForGapNCSG-InfoEUTRA and NeedForGapsInfoNR in CU to DU RRC Information.
  Add the ul-GapFR2-Config IE in the DU to CU RRC Information.
  Add the interFrequencyConfig-NoGap IE in the DU to CU RRC Information.

## Slide 24: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding online sessions and the post-meeting email discussion!
Young Ik Jo (RAN WG3 Secretary)
  For his good support and hard work during the meeting weeks!
Henrik, Jiajun Chen, Jianchen Sun, Hong Wang, Yanshen Liu, Shoki
  For their excellent and hard work on moderating some tough email discussions and good support!
All Rapporteurs and moderators
  For their efforts to R18 WIs/SIs and R17 maintenance!
All RAN3 delegates
  For their positive, constructive and cooperative spirit and patience!