## Slide 1: Proposed NTN Enhancements in Release 19 5/30/23
3GPP TSG RAN Rel-19 Workshop
June 15-June 16, 2023
RWS-230032
Agenda Item: 5

## Slide 2: Proposed NTN Enhancements
Flexible and Relaxed QoS (FRQ)
Regenerative Payloads
Spectrum Sharing with NTN (SSN)

## Slide 3: Motivation for Flexible and Relaxed QoS (FRQ)
To accommodate long propagation delays in a GEO-based NTN, the 3GPP introduced a new 5QI (5G QoS Indicator).
An NTN involves varying propagation delays based on the type of the NTN platform such as ultra-short delays in case of a HAPS, short delays for a LEO satellite, medium delays for a MEO satellite, and long delays for a GEO satellite. An NTN may not be able to meet match the performance of a TN for many different services.
To support many types of services in an NTN, an operator may want to offer services with more relaxed QoS requirements for an NTN compared to a TN. For example, low-resolution videos or reduced-quality voice calls could be offered by an NTN.

## Slide 4: Flexible and Relaxed QoS (FRQ) for the NTN: A Brief Description
Goal: Provide adequate flexibility to service providers to offer diverse services without increasing the number of 5QIs
Use the existing 5QIs as baseline.
Introduce scaling factors for key parameters of a given 5QI such as the error rate and the packet delay
NTN QoS Parameter Value= X* TN QoS Parameter Value.
Example: NTN PLER = X* PLER, where PLER is the normal PLER Packet Loss Error Rate. The TN PLER may be 1% but the relaxed QoS for the NTN is 2%.
Define a suitable range of scaling factors (e.g., X in the example above) that can be used by a service provider to meet the target QoS for their planned services

## Slide 5: Motivation for Regenerative Payloads
A transparent payload is inadequate in providing truly ubiquitous coverage due to the unavailability of a land mass for an NTN-GW (e.g., middle-of-the-ocean coverage).
A transparent payload solution may be less efficient to serve certain scenarios compared to regenerative payload. Regenerative payload provides better routing, benefits low latency use cases, serves geographically challenging locations, and requires less number of NTN-GWs.
A regenerative payload can provide enhanced support for several use cases that can be served by a transparent payload.
Regenerative payloads can enhance resiliency.
Note 1. Optical Inter Satellite Link (ISL) can be considered by the 3GPP.
Note 2. Please note that the 3GPP has previously discussed various regenerative architectures.

## Slide 6: Regenerative Payload Architecture Examples
gNB-DU (including RU) on the payload
Entire gNB (including gNB-DU with RU and gNB-CU) on the payload
Entire gNB and partial 5GC on the payload
Reduces payload complexity
Efficient for interoperability with TN & multi-connectivity
Faster deployment solution for unserved and hard to reach areas by TN
Less work for specification enhancements
Lower latency use cases such as emergency management and edge computing
Disaster relief & Ad hoc networks

## Slide 7: Benefits of Regenerative Payloads
Ubiquitous service for geographically challenging locations where “transparent” payload solution is not feasible
Enables lower latency services and capability to host edge compute in space
Efficient use of service link, and feeder link resources
Possibility of direct device to device connectivity without requiring a ground hop
Easier to support multiple ground core networks operated by different service providers
Fast path mobility
Enhanced support for several use cases: Aeronautical and Maritime Broadband Usage, Agriculture, Automotive (V2X), Maritime, Disaster relief, Emergency and safety, eHealth
Note: For R17 and R18, it was agreed that only the transparent payload would be supported. The transparent payload has performance limitations which could be addressed by a regenerative payload in R19 per 3GPP discussions (e.g., seamless mobility with TN, coverage enhancements, and dynamic capacity management).

## Slide 8: Motivation for Spectrum Sharing
Spectrum will continue to play an important role in 5G-Advanced and 6G.
To enhance performance in both a TN and an NTN, spectrum sharing between a TN and an NTN would be useful.
Scenario 1. There is propagation-based isolation between the outdoor environment and indoor environment. Hence, it may be possible for a low-power indoor wireless system (e.g., in homes and enterprises) to make use of the licensed spectrum typically used by an NTN in such geographic area.
Scenario 2. A given portion of spectrum may not be used all the time in the entire service area of a TN service provider. Such spectrum could be used by a suitable NTN. For example, TN service providers may not be using certain licensed spectrum in remote areas such as mountainous regions or rural areas. An NTN service provider may be able to use such licensed TN spectrum in these remote areas.
We suggest that 3GPP study various spectrum sharing scenarios to determine which scenarios would be feasible.

## Slide 9: Spectrum Sharing: A Brief Description
An intelligent spectrum coordination system can help minimize the probability of any interference resulting from sharing of licensed spectrum.
A central automated spectrum coordination system can facilitate near-real-time spectrum coordination between a TN system and an NTN system.
Sharing of licensed spectrum may (or may not) involve financial arrangements between a TN service provider and an NTN service provider. For example, different entities may compete for a chunk of licensed spectrum offered by a spectrum owner with geography-based and/or time-based usage of licensed spectrum, and a central spectrum coordination system determines which entity can use a given chunk of spectrum.

## Slide 10: Appendix I: Additional Regenerative Payload Architectures
Note. The 3GPP can discuss various architectures and down-select a subset of these for normative work.

## Slide 11: Additional Architectures
eNB on the payload for IoT
(Regenerative Payload)
eNB and Core on Payload for IoT
(Regenerative Payload)
Multi-connectivity
Satellite Backhaul
TN gNB
NTN Platform
NTN-GW
5GC
(Avoid fiber needs in a rural or remote area)