## Slide 1: Considerations on Rel-19 WI on AI/ML for NR air interface
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-230311
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Status of Rel-18 SI on AI/ML for NR air interface
  General aspects of AI/ML framework:
    Good progress on inference-related LCM procedures,
      Functionality-based and Model ID-based LCM are identified.
    Some progress on model monitoring and data collection. Open issues expected to be resolved in August WG meeting.
      Data collection requirements/framework will be considered per use case per LCM purpose (i.e. model training/monitoring/inference)，pending on RAN1 reply LS for further down-selection.
    Limited studies on model transfer and model training.
      Both CP-based and UP-based model transfer are still under estimation in RAN 2. But the feasibility highly depends on RAN1 guidance/requirement.
  Use cases
    Identified 6 sub use cases: CSI compression, CSI prediction, spatial domain beam prediction, temporal beam prediction, direct AI/ML positioning and AI/ML assisted positioning.
    Comprehensive evaluations for the all 6 use cases. Observed performance gain in some scenarios.
    Good progress on the potential specification impacts of 5 sub use cases. But study on AI/ML based CSI prediction only focuses on evaluation yet.
    Two-sided model for CSI compression. One-sided model for the other 5 use cases.
    Evaluations and studies on online training/tuning/updating are not touched in R18.

## Slide 3: Status of Rel-18 SI on AI/ML for NR air interface (Cont’)
  RAN4 status：
    Agreed to study model interference.
    LCM is under discussion.
      Agreed to study model monitoring, model select/switch/activate/deactivate/fallback.
      Training is deprioritized.
      FFS data collection, model update/delivery.
    Agreed to study all 6 sub use cases, and kick off with good progress on performance requirement and core requirement of each case.
      Candidate KPIs for different sub cases are identified.
    Test method for two-sided model is not clear.
      Introduction of reference model is a challenge work in RAN4.
      How to test LCM and ensure the practical effectiveness of AI/ML solutions remains more study.

## Slide 4: Rel-19 RAN1-led WID proposal
  In the Rel-18 SI
    The benefits of AI/ML operations for identified sub use cases are justified by comprehensive studies and extensive evaluations.
    Some basic LCM procedures are well studied and identified.
  A RAN1-led WI in Rel-19 is proposed, with the following focuses:
    Specify the basic components of general AI/ML LCM which were well-identified in Rel-18.
    All 6 representative sub use cases studied in Rel18 are supported.
    Specify RAN 4 requirements.

## Slide 5: R19 RAN1-led WID – LCM framework
  Specify the basic components of general AI/ML LCM that are applicable to all representative sub use cases studied in Rel-18:
    Both functionality-based and model ID-based LCM framework are supported.
      Based on offline model identification (Type A)
    Focus on model inference and performance monitoring-related procedures.
    Data collection for inference and monitoring are supported.
  Offline model training is assumed.
    No dedicated spec enhancement for online training.

## Slide 6: R19 RAN1-led WID – Use cases
  For each sub use case,
    Specify use case specific signaling/procedure enhancements on measurement, reporting for model inference and the subsequent operations (if any)
      E.g., the interface type, format, content, quantization and model input/output, if needed.
    Specify use case specific signaling/procedure enhancements for LCM procedures, especially detailed design on performance monitoring and subsequent operations, e.g., model activation/deactivation, switching, update, fallback.
  Specify signaling/procedures for two-sided AI model
    For CSI compression.
  Specify signaling/procedures for one-sided AI model
    Both UE-side model and NW-side model are supported.
    For CSI prediction, spatial domain beam prediction, temporal beam prediction, direct AI/ML positioning and AI/ML assisted positioning.

## Slide 7: R19 RAN1-led WID – RAN4 requirements
  Support all representative sub use cases studied in Rel-18.
  Specify KPIs design and tests on performance requirement for each use case.
    Down select and specify KPIs for each use case.
    Specify test condition/procedure/scheme for use cases, e.g. dataset/configuration/scenario.
  Core requirement tests for each use case, especially for LCM related core requirement tests.
    Identify LCM functionalities that should be under test in RAN4.
    Specify core requirements and test methodologies.
  Address the testability issue on two-sided model test.
    Specify the framework, condition and methodology.
    Confirm the construction/acquisition schemes for reference models, including reference UE side model and reference NW side model.