## Slide 1: Motivation for R19 enhancement of NR SL Relay
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-230314
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Part-1: UE-based Relay in LTE

## Slide 3: Background: R13 eD2D L3 Relay
SID/WID: SP-140386 (SA1), SP-140385 (SA2), RP-142311 (RAN)
Time: 2015~2016
Objective: Support the extension of network coverage using L3-based UE-to-Network Relays, including service continuity (if needed), based on Release 12 D2D communication, considering applicability to voice, video. [RAN2, RAN1, RAN3].

## Slide 4: Background: R15 FeD2D L2 Relay
SID/WID : SP-160511 (SA1), SP-160961 (SA2), RP-170295 (RAN)
Time: 2016~2017
Objective: Study the possibility of a common solution supporting the following use cases:[RAN2]
  i. UE to network relaying over non-3GPP access (Bluetooth/WiFi).
  ii. UE to network relaying over LTE sidelink.
  iii. Unidirectional and bidirectional UE to network relay.
3GPP based UE-to-UE link

## Slide 5: Background
In LTE, although the UE-based U2N relay has been specified (only in R13), it is quite limited in the sense that
  Single UE-to-UE protocol (i.e., LTE sidelink)
  Without scalability (single hop, single path)
  Supporting limited type of traffic (Public Safety oriented)

## Slide 6: Part-2.1: UE-based Relay in R17/R18 NR

## Slide 7: R17 SL-Relay: L2/L3 U2N Relay
SID/WID : SP-200972 (SA2), RP-212601 (RAN)
Time: 2019~2022
Objective: Study mechanism(s) with minimum specification impact to support the SA requirements for sidelink-based UE-to-network and UE-to-UE relay, while WI focused on U2N only, covering both layer-3 relay and layer-2 relay..
L2 UE-to-NW Relay
L3 UE-to-NW Relay (non-N3IWF scheme)

## Slide 8: R18 SL-Relay: L2/L3 U2U Relay
SID/WID : SP-211653 (SA2), RP-223501 (RAN)
Time: 2022~2023
Objective: WI focused on U2U, covering both layer-3 relay and layer-2 relay. Plus enhancement of L2 U2N Relay, in terms of service-continuity and multi-path Relay.
L2 UE-to-UE Relay
L3 UE-to-UE Relay

## Slide 9: R17/18 SL-Relay
Progress till now
  Basic component for both U2U and U2N, and both L2 and L3 relay
  U2N:
    Allowing multi-path (1direct+1indirect, intra-gNB, PC5/Ideal connection),
    Limited to single-hop, unicast
  U2U: Limited to single-path, single-hop, unicast

## Slide 10: Part-2.2: UE-based Relay in R19 NR

## Slide 11: R19 SL-Relay
Single-hop Relay => Multi-hop Relay
Basic Multi-Path => Advanced Multi-Path
Single-Carrier relaying => Multi-Carrier relaying

## Slide 12: R19 SL Relay: Multi-Hop (1/3)
In 22.261, KPI for multi-hop UE-to-Network Relay has been provided
Scenario | Max. data rate (DL) | Max. data rate (UL) | End-to-end latency (note 7) | Area traffic capacity (DL) | Area traffic capacity (UL) | Area user density | Area | Range of a single hop (note 8) | Estimated number of hops
InHome Scenario (note 1) | 1 Gbit/s | 500 Mbit/s | 10 ms | 5 Gbit/s/ home | 2 Gbit/s /home | 50 devices /house | 10 m x 10m – 3 floors | 10 m indoor | 2 to 3
Factory Sensors (note 2) | 100 kbit/s | 5 Mbit/s | 50 ms to 1 s | 1 Gbit/s /factory | 50 Gbit/s /factory | 10000 devices /factory | 100 m x 100 m | 30 m indoor / metallic | 2 to 3
Smart Metering (note 3) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /hectare | 200 x 100 bytes / 15 mins /hectare | 200 devices /hectare | 100 m x 100 m | > 100 m indoor / deep indoor | 2 to 5
Containers (note 4) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 15000 x 100 bytes / 15 mins /ship | 15000 x 100 bytes / 15 mins /ship | 15000 containers /ship | 400 m x 60 m x 40 m | > 100 m indoor / outdoor / metallic | 3 to 9
Freight Wagons | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /train | 200 x 100 bytes / 15 mins /train | 120 wagons /train | 1 km | > 100 m outdoor / tunnel | 10 to 15
Public Safety (note 5) | 12 Mbit/s | 12 Mbit/s | 30 ms | 20 Mbit/s /building | 40 Mbit/s /building | 30 devices /building | 100 m x 100 m – 3 floors | > 50 m indoor (floor or stairwell) | 2 to 4
Wearables (note 6) | 10 Mbit/s | 10 Mbit/s | 10 ms | 20 Mbit/s per 100 m2 | 20 Mbit/s per 100 m2 | 10 wearables per 100 m2 | 10 m x 10 m | 10 m indoor / outdoor | 1 to 2

## Slide 13: R19 SL Relay: Multi-Hop (2/3)
Coverage Enhancement
  Coverage Enh necessity for FR1, e.g., range extension without need for LF spectrum
  Coverage Enh necessity for FR2, e.g., 8-hop @ 24GHz = 2-hop @ 5.9GHz
  APP-level solution is infeasible due to APP-level Re-processing
    Security concern
    Additional latency
    Out of network control
Chart: Range vs. Hop
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
2 | 944 | 1888 | 2832 | 3776 | 4720 | 5664 | 6608 | 7552 | 8496 | 9440
3.5 | 539.4286 | 1078.8571 | 1618.2857 | 2157.7143 | 2697.1429 | 3236.5714 | 3776 | 4315.4286 | 4854.8571 | 5394.2857
5.9 | 320 | 640 | 960 | 1280 | 1600 | 1920 | 2240 | 2560 | 2880 | 3200
24 | 78.6667 | 157.3333 | 236 | 314.6667 | 393.3333 | 472 | 550.6667 | 629.3333 | 708 | 786.6667
61 | 30.9508 | 61.9016 | 92.8525 | 123.8033 | 154.7541 | 185.7049 | 216.6557 | 247.6066 | 278.5574 | 309.5082

## Slide 14: R19 SL Relay: Enhanced Multi-Path (1/3) General
R18 Relay is limited to
  1-direct + 1-indirect (PC5, or non-3GPP Ideal connection)
  Intra-gNB multi-path
  SP-from/to-MP switching limited to intra-gNB
  No MP-to-MP switching

## Slide 15: R19 SL Relay: Enhanced Multi-Path (2/3) Topology
Enh of indirect leg: more than 1 indirect leg, MP w/o direct leg
  => To support simultaneous emergency + non-emergency traffic for OOC UE
  => To benefit for the UEs out of direct coverage, and to enhance the assistance degree from the indirect path
 | R18 | R19
Topology | 1-direct + 1-indirect for intra-gNB | 1-direct + >1-indirect
 |  | 1-indirect + >=1-indirect

## Slide 16: R19 SL Relay: Enhanced Multi-Path (4/3) Service-Continuity
Enh for inter-gNB: inter-gNB SP/MP-2-MP switching, MP over 2 gNB:s
  => to support continuity of MP when moving across gNBs
  => advanced mobility tool, e.g., group-HO.
From row to column | SP, direct | SP, indirect | MP
SP, direct | Legacy HO | R17 (intra-gNB) R18 (inter-gNB) | R18 (w/o direct leg change) R19 (w/ direct leg change)
SP, indirect | R17 (intra-gNB) R18 (inter-gNB) | R18 | R18 (w/o indirect leg change) R19 (w/ indirect leg change)
MP | R18 (w/o direct leg change) R19 (w/ direct leg change) | R18 (w/o indirect leg change) R19 (w/ indirect leg change) | R18 (w/o direct change, w/ indirect change, R18 w/ direct change, w/o indirect change R19 w/ both direct change and indirect change)

## Slide 17: R19 SL Relay: CA-Related Enh
SL CA was specified in R18, without considering relay-specific enhancement, e.g.,
  How for relay UE to broadcast discovery message over multi-carrier of PC5 interface
  How for remote UE to operate Uu-PDCP-duplication over multiple PC5 carriers
It helps to further boost PC5-based U2N Relay capability.

## Slide 18: Summary
R18 Enhancement aims at a further enhanced UE-based relay architecture which targets at
  Extended from single hop to multi-hop
  Enhanced multi-path relay
  Solving R17/18 left-overs