## Slide 1: Further enhancement for SON/MDT in Rel-19
June 15, 2023
RWS-230392
Agenda Item: 5
Source: Lenovo
Document for: Discussion
3GPP TSG RAN Release 19 workshop
Taipei, June 15-16, 2023

## Slide 2: Motivations
  In Rel18, SON/MDT enhancements are specified for:
  Inter-RAT SHR, SPR;
  Inter-system handover for voice fallback, CPAC, and fast MCG recovery;
  RA report;
  NPN;
  NR-U;
  Signaling based logged MDT override protection.
  In Rel-19, we need to further enhance SON/MDT framework to improve network performance or deployment.
  In R19, SON/MDT enhancements should mainly focus on new features introduced in Rel-17 and Rel-18.

## Slide 3: Use Cases for SON Related Enhancements (1)
  MRO for LTM:
  Enable LTM failure type detection and mobility optimization in source DU.
  Enable RA failure reporting and optimization for early TA acquisition.
  Enable MRO for LTM based fast failure recovery.
  MRO for selective activation of SCG:
  Enable SPR for consecutive near failure events in subsequent CPC.
  Enable failure type analysis between MN and SN(s).
  MRO for CHO with candidate SCGs to enable the following cases:
  Case 1: failure cases for CHO with candidate SCGs:
    1a: both CHO and CPAC execution conditions are fulfilled;
    1b: CHO execution condition is fulfilled but CPAC execution condition is not fulfilled.
    1c: CHO execution condition is not fulfilled but CPAC execution condition is fulfilled.
    1d: both CHO execution condition and CPAC execution condition are not fulfilled.
  Case 2: near failure successful case for CHO with candidate SCGs.
  Case 3: CHO-only or legacy CHO with SCG is performed in case that both CHO-only or legacy CHO with SCG and CHO with candidate SCGs are configured.

## Slide 4: Use Cases for SON Related Enhancements (2)
  MDT enhancements for NR MBS in idle/inactive
  The problem of verifying the performance of DL transmissions w/o UL feedback was discussed in LTE in the context of eMBMS and as solution the collection of MBMS related measurements using MDT was agreed in Rel-12.
  In view of the LTE solution for eMBMS, a similar solution can be adopted for MBS broadcast sessions by reusing the NR MDT functionality as much as possible. For example, the UE may be configured to log MBS related measurement information of broadcast sessions in RRC_IDLE and/or RRC_INACTIVE.
  MRO for NTN CHO:
  Enable MRO for timing and distance-based CHO;
  SHR for timing and distance-based CHO.
  SON for multi-SIMs:
  RLF related handling during ‘Leaving’ event (T346g).
  MDT for SDT
  Event reports for SDT resource selection.
  Rel-18 Leftovers
  MRO for NR-U in MR-DC scenarios, MRO for (NG)EN-DC CPAC, and etc.

## Slide 5: Summary
  The following use cases should be considered in Rel-19 SON/MDT enhancements WI:
  MRO for LTM;
  MRO for selective activation of SCG;
  MRO for CHO with candidate SCGs;
  MDT enhancements for NR MBS in idle/inactive;
  MRO for NTN CHO;
  SON for multi-SIMs;
  MDT for SDT;
  Rel-18 leftovers, e.g., MRO for NR-U in MR-DC scenarios, MRO for (NG)EN-DC CPAC.

## Slide 6: Thanks
thanks