## Slide 1: Views on Further Study on AI/ML for NR Air Interface Enhancement in Rel-19
3GPP TSG RAN Release 19 workshop RWS-230395
Taipei, June 15 –16, 2023
Agenda Item: 5
Source: Lenovo
Document for: Discussion

## Slide 2: Current status in Rel-18 SI: general aspects
A general AI/ML framework
  Include model training, model management, data collection, model inference and model storage
Network-UE collaboration levels
  Level x: No collaboration
  Level y: Signaling-based collaboration without model transfer
  Level z: Signaling-based collaboration with model transfer
Life-cycle management (LCM) principles
  Functionality-based and Model-ID-based LCM
    Different manageable granularity for UE-side or UE-part of two-sided models, based on identified configurations.
  Relevant operations and functions
    Performance monitoring, activation/deactivation, selection, switching, updating and fallback.
Configuration parameters set A
Application conditions set A
Functionality A
Configuration parameters set B
Application conditions set B
Functionality B
AI/ML-enabled UE Feature
Description
Configuration
Conditions
Description
Configuration
Conditions
AI/ML-enabled UE Feature
Model 1
Model 2
Description
Configuration
Conditions
Model 3
Data collection
Inference
Management
Training data
Output for Monitoring
Selection/(de)activation
/switching/fallback
Model Training
Performance feedback/
Retraining Request
Trained/updated model
Monitoring Data
Inference data
Model Storage
Model transfer/delivery request
Model transfer/delivery

## Slide 3: Current status in Rel-18 SI: sub use cases
CSI feedback enhancement
  Spatial-frequency domain CSI compression using two-sided AI model
  CSI prediction using one-sided model
Beam management (BM)
  BM-Case1: Spatial-domain DL Tx beam or beam pair prediction
  BM-Case2: Temporal DL Tx beam or beam pair prediction
Positioning accuracy enhancement
  Direct AI/ML positioning
  AI/ML assisted positioning
Evaluations
  The RS and CSI feedback overhead reduction can be observed with some configurations and simulation assumptions.
    CSI feedback compression, BM-Case1
  The estimation accuracy can be improved with some configurations and simulation assumption.
    Positioning and CSI prediction
Potential specification impact
  Model inference
  Data collection
    E.g., label data for training and monitoring
  Performance monitoring
Observation 1: The number of sub use cases could be too large for the normative stage.
Observation 2: Some features in AI/ML are deprioritized, such as model transfer, online training.

## Slide 4: General views on AI/ML for air interface enhancement in Rel-19
The next stage of Rel-18 SI on AI/ML for NR air interface enhancement can include two items:
  Rel-19 WI: AI/ML for NR air interface
  Rel-19 SI: Study on AI/ML for NR air interface – Phase 2
Rel-18 SI: Study on AI/ML for NR air interface enhancement
General aspects LCM Sub use cases CSI feedback enhancement Beam management Positioning accuracy enh. Performance evaluation Specification impact
Rel-19 WI: AI/ML for NR air interface
Specify signaling and procedures to support LCM, e.g., identification, activation/deactivation. Specify relevant AI/ML operations on selected sub use cases, e.g., data collection, model inference, performance monitoring and fallback schemes
Rel-19 SI: Study on AI/ML for NR air interface – Phase 2
Remaining issues deprioritized in Rel-18, e.g., model transfer, online training Further study on some sub use cases in Rel-18, e.g., CSI prediction Study on some new use cases, e.g., mobility

## Slide 5: Rel-19 WI: AI/ML for NR Air Interface
Motivation
  Specify the relevant procedures to support AI/ML functionality/models
  Specify the AI/ML-related operations on the selected sub use cases with representative model deployment and observed enough gains from Rel-18 study.
Objectives
  Specify signaling and procedures to support AI/ML functionality-based/model-ID-based LCM
    LCM operations, e.g., functionality/model identification, switching, activation/deactivation, selection, etc.
  Specify the below representative sub use cases:
    Spatial-Frequency domain CSI compression with two-sided model
    Spatial domain beam prediction with single-sided model
    Both Cases 2 and Case 3, including direct AI/ML and AI/ML-assisted Positioning
  Specify the support on relevant AI/ML operations, at least including
    Efficient methods for data collection, e.g., training and monitoring data
    Performance monitoring procedure, e.g., configuration, trigger and report and potential fallback.
    Model inference, e.g., configuration of model input for different conditions

## Slide 6: Rel-19 SI: Study on AI/ML for NR Air Interface – Phase 2
Motivation
  Remaining issues from Rel-18 SI, e.g., model transfer, online training and two-side training.
  More potential use cases can be further studied to explore more potential benefits from AI/ML, e.g., CSI feedback compression with multi-TRP, mobility enhancement and interference management.
Objectives
  Study the specification impacts to support more potential AI/ML functions
    Enhancement to support model transfer, online training, two-side training and tuning
    Collaborative/distributed model training and inference
  Further study the performance and specification impact of new use cases in Rel-19
    CSI feedback compression for multi-TRP scenario
    Mobility enhancement, e.g., assist parameter adjustment, reduce RLF/HO failure, target cell prediction
    Interference management, e.g., interference prediction and interference avoidance through intelligent resource allocation

## Slide 7: Summary
In Rel-19, the study on AI/ML for NR air interface enhancement can include two items, one is WI to specify relevant AI/ML operations, the other is SI to further study AI/ML for more use cases.
Rel-19 WI: AI/ML for NR air interface
  Specify the relevant procedures to support AI/ML functionality/models
  Specify relevant procedures on the selected sub use cases with representative model deployment and observed enough gains from Rel-18 study.
Rel-19 SI: Study on AI/ML for NR air interface – Phase 2
  Study remaining issues from Rel-18 SI, e.g., model transfer, online training
  Study more potential use cases can be further studied to explore more potential benefits from AI/ML, e.g., CSI feedback compression with multi-TRP, mobility enhancement and interference management