## Slide 1: Discussion on Reconfigurable Intelligent Surface (RIS) in RAN Rel-19
3GPP TSG RAN Release 19 workshop RWS-230396
Taipei, June 15 –16, 2023
Agenda Item: 5
Source: Lenovo
Document for: Discussion

## Slide 2: Motivation
RIS is a planar meta-surface equipped with a large number of passive reflecting elements connected to a smart controller to independently control phase shift and/or amplitude attenuation (termed as “reflection coefficient”) to the incident signal at each reflecting element in real-time.
  RIS types: passive RIS without RF chain or active RIS with RF
  RIS operating mode: reflection, refraction and absorption mode.
RIS can be deployed to improve the communication performance via smart adjusting the coefficients in following scenarios with lower cost than NCR
  Cell-edge users’ throughput, indoor coverage
  Create the cascaded path to users in a coverage hole
  Increase revenue opportunities by enabling new services that require high data rates
Reflection mode
Refraction mode
Absorption mode

## Slide 3: Network-Controled Repeater (NCR) in Rel-18
In Rel-18, a network-controlled repeater was studied as an enhancement over conventional RF repeaters with the capability to receive and process side control information from the network.
  Side control information, including beam information, ON-OFF information and TDD DL-UL configuration, etc., could allow a network-controlled repeater to perform amplify-and-forward operation in a more efficient manner.
RIS can potentially provide further lower cost to improve coverage with enhanced side control information definition and transmission, according to the operation mode.
  E.g., reflect coefficients indication, mode switching and association with other techniques.

## Slide 4: Controlling type of RIS
Network-controlled RIS
  The network determines the control information to control and configure RIS.
Network-assisted RIS
  The network provides the assistance information to the RIS controller, which can be either deployed and owned by the network or separated deployed as a 3rd party component.
Standalone RIS
  The RIS controller, which can be pre-configured by the network or a 3rd party component, determines the control information.
gNB-controlled RIS
  The gNB determines the control information and configures the RIS for a specific operating frequency range.
UE-controlled RIS
  The UE determines the control information and configures the RIS for a specific operating frequency range.

## Slide 5: Typical use cases of RIS
Coverage enhancement
  Establish line-of-sight paths between access points, RIS, and terminals
  Improve coverage in weak areas
Beam management
  Manage different groups of elements for different users
  Enhanced signal strength and less power consumption compared to massive MIMO
  As an alternative solution to multi-TRP deployment
Positioning
  More flexible and lower cost compared to deploying BS
  Higher spatial resolution and positioning accuracy
Sensing capabilities in ISAC systems
  Establishing LoS link for NLOS areas
  Providing extra LoS reflected link for different angles
Energy Saving
  Reducing network energy consumption
  Improving the energy efficiency of users considering the uplink transmission
gNB
User
RIS
gNB
User
gNB
User
RIS
Target
Coverage enhancement
Associated with ISAC
Beam management

## Slide 6: Channel modelling considerations
A free-space path loss considering far-/near-field can be derived as
The cascaded channel of gNB-RIS-UE is modeled as the product of Rician fading
Near-field vs. Far-field: different path-loss models due to differences in EM fields
  Far-field model
    Transmitter's spherical wave approximated as a plane wave at receiver side
    Distances can be modeled as a single entity
    Phases need to be modeled separately
  Near-field case:
    Different phased array elements need to be modeled separately in terms of short distances and phase shifts.
Outage performance of a link with RIS via numerical calculation and simulation.

## Slide 7: Potential air interface enhancement
Relevant procedures to support RIS deployment
  Codebook design for reflection coefficients
  Side control information delivery
  CSI feedback enhancement
Potential air interface enhancement with RIS
  Initial access procedure
  Beam management
  Positioning accuracy improvement
  Interference management
RIS controller
RIS reflector
gNB
UE
gNB-controlled RIS
Control information
DL
DL
UL
UL

## Slide 8: Summary & Proposals
Motivation
  Study the feasibility of RIS deployment in RAN to efficiently improve the communication performance, e.g., coverage enhancement, energy saving.
Objectives
  Discussion on use cases and RIS operation modes
    E.g., gNB-controlled or UE-controlled to improve coverage
  Propagation channel modeling with RIS involved
    Extend the channel model in TR 38.901 to support the reflection/refraction and near/far field
  Potential air interface enhancement with RIS-assisted communication
    E.g., initial access, beam management
  KPI and evaluation methodology
    E.g., cell throughput, coverage and energy efficiency
  Side control information
    E.g., content and transmission scheme