## Slide 1
RWS-230439
Views on Ambient IoT
5G-Advanced Evolution: Rel-19
  —
  3GPP RAN Release 19 Workshop, 15th – 16th June 2023, Taipei

## Slide 2: Views on Ambient IoT
Motivation
      Motivation :
        Support of battery-less devices with low data throughput for sensors or asset tracking applications
      Scope :
        Ambient IoT Study Item with focus on the following device-topology combinations (based on device categories and topologies from TR 38.848):
          Topology 3 with all device categories (A, B, and C)
          Topologies 1, 2 and 4 with device C, full-duplex is not viable with consumer price UEs
        Also study full-duplex cross-band operation as a possible alternative to backscattering (at least for Topologies 2 and 4)
RWS-230439

## Slide 3: Views on Ambient IoT
Backscatter Communication
        General Thoughts on Backscattering:
      Theoretical limits: Backscatter transmission has the potential to transmit data over several hundreds of meters with suitable data rates. Bistatic setups (like Topology 3) and Ambient Backscattering using broadcast signals like DAB or DVB-T as signal of opportunity can even achieve long-range transmission over multiple kilometers. An in-depth investigation of the theoretical limits of backscatter communications is given in [1].
      Localization of backscatter devices: Backscattered signals are usually very weak. However, monostatic setups (like Topology 1) have an advantage for localization as there will be no phase noise in the received backscatter signal (if the same oscillator is used for transmission and sampling by the receiver).
      Full-duplex transmission and carrier signal suppression: Backscattering in a monostatic setup requires full-duplex transmission capabilities with a sophisticated carrier signal suppression at the receiver, which is not suitable for Topology 4 with consumer price UEs.
      Potential Advantages of a Novel Backscatter Air Interface over RFID-Systems:
      Tag reading rate: The tag reading rate in RFID systems is restricted by a frame-slotted ALOHA protocol that prohibits parallel tag-reads. A 3GPP Ambient IoT protocol could achieve significantly higher reading rates, for example by receiving several backscattered signals in parallel.
      Localization: With a novel backscatter air interface, there are possibilities for increasing the accuracy of localization or motion detection.
RWS-230439
      [1]: C. Korn, J. Robert, T. Dräger, ” Theoretical Limits of Backscatter Communications”, arxiv pre-print, https://arxiv.org/abs/2302.13958

## Slide 4: Views on Ambient IoT
Alternative to Backscatter: Cross-band Operation with Energy Harvesting
Full-duplex cross-band operation allows a very power-efficient communication without requiring real full-duplex capable receivers.
      For active ultra-low power radio transmission, one of the biggest power consumers is the crystal oscillator that is required to generate the RF signal.
      The use of a crystal oscillator can be avoided by transmitting a clock reference signal to the Ambient IoT device.
      The Ambient IoT device then transmits data in a higher frequency band using a clock reference that is based on the reference signal.
      The cross-band Ambient IoT device is powered by energy harvesting and requires significantly less power than devices with crystal oscillator.
      Cross-band operation is particularly relevant for Topologies 2 and 4, where the receiver might not be capable of full-duplex operation with sophisticated carrier signal suppression.
Exemplary implementation of a full-duplex cross-band Ambient IoT device with energy harvesting from the RF field
RWS-230439