## Slide 1: WF on LAA DRS design and transmission timing
NTT DOCOMO, Panasonic, Sharp, Huawei, HiSilicon, ITRI
R1-154897
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th – 28th August 2015
Agenda item 7.2.4.2.1

## Slide 2: Background
During LAA SI, following agreements were made.
  DRS design should allow DRS transmission on an LAA SCell to be subject to LBT
  Consider the following 2 options for the transmission of DRS within a DMTC window if LBT is applied to DRS
    Alt1: Subjected to LBT, DRS is transmitted in fixed time position within the configured DMTC
    Alt2: Subject to LBT, allow the DRS to be transmitted in at least one of different time positions within the configured DMTC
      Note: The number of different time positions should be restricted
      Note: One possibility is one time position in the subframe
    Modifications to Rel-12 DMTC configuration are FFS
  Note: this does not preclude the possibility to allow other DRS transmissions outside of the configured DMTC
According to evaluation results in R1-154264 and R1-154767, it is observed that the DRS transmission probability of Alt.2 is much higher than that of Alt.1

## Slide 3: Updated proposal
Subject to LBT, allow the DRS without PDSCH to be transmitted in at least one of different time positions within the configured DMTC
  FFS: Different time position of the case of DRS and PDSCH are in the same DL transmission bursts
  DRS occasion duration which doesn’t include potential initial signal part is less than 1 ms
    FFS: Possible DRS occasion duration
  DRS occasion is time-continuous and contains at least PSS/SSS/CRS
    FFS: the number of CRS ports
  Allow DRS transmission in subframe other than #0 and #5
  Candidate position of DRS in each subframe within DMTC is fixed relative to subframe timing
  Following alternatives can be considered to solve sequence generation issue for SSS/RS in subframe other than #0/#5
    Alt. 1: Generate SSS/RS sequences according to the subframe index of DRS and UE identifies the subframe index of DRS by the sequence.
    Alt. 2: Generate SSS/RS sequences irrespective of the subframe index of DRS and UE doesn’t need to identify the subframe index of DRS for RRM measurement.
    Alt. 3: Generate SSS/RS sequences irrespective of the subframe index of DRS and UE identifies the subframe index of DRS by signaled information in DRS.
    FFS: other alternatives

## Slide 4: Proposal (clean ver.)
Subject to LBT, allow the DRS without PDSCH to be transmitted in at least one of different time positions within the configured DMTC
  FFS: Different time position of the case of DRS and PDSCH are in the same DL transmission bursts
  DRS occasion duration which doesn’t include potential initial signal part is less than 1 ms
    FFS: Possible DRS occasion duration
  Allow DRS transmission in subframe other than #0 and #5
  Candidate position of DRS in each subframe within DMTC is fixed relative to subframe timing
  Following alternatives can be considered to solve sequence generation issue for SSS/RS in subframe other than #0/#5
    Alt. 1: Generate SSS/RS sequences according to the subframe index of DRS
    Alt. 2: Generate SSS/RS sequences irrespective of the subframe index of DRS
    FFS: other alternatives