## Slide 1: Way Forward on MUST Transmission
MediaTek, ASUSTEK COMPUTER (SHANGHAI), CHTTL, Huawei, HiSilicon, HTC, III, ITRI,
NTT DOCOMO INC., NTU, Sharp, ZTE
R1-165797
3GPP TSG-RAN WG1 #85
Nanjing, China, 23rd – 27th May 2016
Agenda item 6.2.4.1

## Slide 2: Proposals
If QPSK is used for MUST-far user and there are multiple power ratios, the power ratios are selected from the union of the sets A and B
  Set A is a finite subset of {x: 0.6 <= x <= 0.75}. FFS on its elements
  B={0.7529, 0.7619, 0.8, 0.85, 0.875, 0.9, 0.95}
    0.7529, 0.7619 and 0.8 correspond to 256QAM, 64QAM and 16QAM composite constellations, respectively
  The following numbers of power ratios are considered for further down-selection
    3, 4, 7 and 8
The selected power ratios can be different for different combinations of MUST-near UE and MUST-far UE modulation orders

## Slide 3: Appendix
Minimum distances of any two points in constellation points