## Slide 1: WF on OTDOA enhancements for FeMTC
Ericsson, Sony, Qualcomm, ZTE, ZTE Microelectronics, Nokia, ASB, Verizon
R1-1613541
3GPP TSG RAN WG1 Meeting #87
Reno, Nevada, USA, 14th – 18th Nov 2016
Agenda item 6.2.8.3

## Slide 2: Background
RAN1#86bis agreements:
  For Rel-14 feMTC OTDOA positioning reference signal, enhancements to the legacy LTE PRS patterns and sequences can be considered but need to be justified by significant performance improvement compared to legacy
    Strive for the possibility for the legacy PRS REs to overlap with the Rel-14 PRS REs
  Rel-14 PRS configuration includes
    All legacy parameters, i.e., bandwidth, periodicity, subframe offset, number of consecutive subframes, etc.
    FFS transmission in invalid subframes
    Sets of values of the parameters are FFS
    Determination of frequency location remains FFS
    Details of Rel-14 PRS configuration parameter settings are FFS
    Details of Rel-14 PRS muting pattern are FFS
    FFS how many Rel-14 PRS configurations are needed per cell
    FFS how many Rel-14 PRS configurations are needed per UE
  RSTD measurement of PRS in different sets of PRBs in the frequency domain is supported
    FFS details
  Frequency hopping of PRS in OTDOA is supported.
    Configurations and details are FFS

## Slide 3: Background
The OTDOA positioning performance for BL/CE UEs with reduced receiver bandwidth and single receive antenna can benefit from PRS transmissions that are more dense in the time domain than what would typically be needed for non-BL UEs
  Allowing PRS transmissions with different signal bandwidths in the same LTE carrier can keep a low PRS overhead while supporting OTDOA for UEs with different maximum receiver bandwidths
Rel-13 allows configuration of valid and invalid BL/CE subframes using a bitmap parameter of length 10 or 40 bits, corresponding to 10 or 40 subframes
  It may be beneficial to allow PRS periodicities of 40 ms (perhaps also 10 and 20 ms)
RAN1 has agreed that PRS frequency hopping should be supported
  It may be beneficial to allow one of the PRS frequency locations to be in the legacy center position even when frequency hopping is used

## Slide 4: Proposals on PRS configurations
PRS bandwidths include {1.4MHz, 3MHz, 5MHz, 10MHz, 15MHz, 20MHz}
  No change w.r.t. legacy LTE PRS bandwidths
  One cell can be configured with multiple PRS bands with up to [3] PRS bandwidths; each band is associated with a set of configuration parameters including PRS configuration index, number of PRS subframes per occasion, muting pattern, and optionally frequency hopping parameters
Supported legacy PRS periodicities are {160, 320, 640, 1280} subframes that are jointly signaled with starting subframe offsets in PRS configuration indices
  No change w.r.t. legacy LTE PRS indices
Supported number of PRS subframes per PRS occasion are [{1, 2, 4, 6, 10, 20, 40, 80, 160}] subframes
Reuse LTE PRS muting mechanism with a bit string of {2, 4, 8, 16} bits, with each bit applied to one legacy PRS period
  No change w.r.t. legacy LTE PRS muting pattern
Add additional configuration parameters to support more frequent PRS transmissions and PRS frequency hopping
FFS: Legacy PRS configuration (including R14 enhancements) is also delivered to (F)eMTC UEs

## Slide 5: Proposals on PRS periodicity
To support more frequent PRS transmission in time, add the following parameters to support multiple PRS occasions in a PRS period
  PRS occasion interval in a PRS period: {10, 20, 40, 80} subframes
    If this is not configured, there is only one PRS occasion in a PRS period.
  FFS: A finer muting pattern applied to PRS occasions in a PRS period
    The muting of the first PRS occasion in a PRS period follows the existing PRS muting
Configuration example: 3 configurations with same configuration index 40 (i.e., 160ms period with 40 starting SFs offset)
  Configuration 1: 20MHz, 1 SF per occasion, PRS occasion interval NOT configured
  Configuration 2: 5MHz, 2 SF per occasion, 80ms PRS occasion interval
  Configuration 3: 1.4MHz, 6 SF per occasion, 40ms PRS occasion interval
160ms
80ms
40ms
Offset: 40ms

## Slide 6: Proposals on PRS frequency hopping
If activated, PRS frequency hopping is configured with the following parameters (similar to Rel-13 eMTC FH):
  Number of bands for frequency hopping X: {2, 4}
    The first band is in the center
  The positions of the remaining X-1 bands FFS (choose option A or option B or option C)
    Option A: The position of each of X-1 bands is indicated separately: narrowband {0,1,…,max-1}
    Option B: The position of the first of X-1 bands PLUS frequency hopping offset
      The position of the first of X-1 bands: narrowband {0, 1, …, max-1}
      Frequency hopping offset: {1, 2, …, max} narrowbands
    Option C: Frequency hopping offset relative to the first band of X bands: {1, 2, …, max} narrowbands
  Frequency hopping interval:
    Option A: {1, 2, 4, 8} SFs for FDD and {1, 5, 10, 20} SFs for TDD
    Option B: one PRS occasion
  FFS: The hopping pattern starts in every radio frame fulfilling SFN mode 8 = 0
  FFS: The same precoder is used within a frequency hopping interval but the precoder could be different across different frequency hopping intervals
160ms
40ms
Offset: 40ms
FH starts
FH starts
FH starts
FH starts