## Slide 1: WF on NR RRM Measurements
AT&T, NTT DOCOMO, Orange
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th –18th November 2016
Agenda: 7.1.2.6
R1-1613554

## Slide 2: Motivation
To ensure forward compatibility and flexible network deployment, NR should avoid the transmission of ‘always on’ signals and channels which have fixed time/frequency resources
The transmission of the RS used for measurement and subsequent report may be configured periodically or instead transmitted “on-demand,” at a different time scales to support different levels of mobility or link management supported by the network which can also be UE-specific.
In addition, the frequency resources used for RRM measurement (e.g. measurement bandwidth) may also be configurable and adapted by the network which can support numerology multiplexing and LTE/NR coexistence.

## Slide 3: Proposal
NR should support adaptation and network indication of the timing for resources used for RRM measurements and reports.
  FFS: UE-specific or cell-specific indication
NR should support semi-static (e.g. RRC configured) adaptation/configuration of the RRM measurement bandwidth.
  FFS: dynamic adaptation/configuration
RAN1 should study mechanisms to support adaptation and configuration of the time/frequency resources used for RRM measurements for both ‘CONNECTED’ and non-‘CONNECTED’ mode UEs.
It is up to RAN4 for determining requirements regarding the extent the UE can restrict its measurement to a subband of the configured bandwidth