## Slide 1: WF on NR Transmission Mode
Intel Corporation, AT&T, Samsung, LG, Huawei
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th –18th November 2016
Agenda: 7.1.3.1
R1-1613583

## Slide 2: Introduction
In LTE, transmission mode is used to predetermine values of many parameters such as DCI format, RS and CSI measurement/reporting method and transmission scheme.
In NR, dynamic adaptation between different transmission schemes are desirable to support various 5G use cases efficiently.
In order words, flexible configuration of different parameters should be supported.

## Slide 3: Proposal
Define two sets of transmission parameters, where
  Transmission parameter set 1: parameters configured by higher layer (FFS: L2 or L3)
    E.g. QCL
    For default transmission scheme, specify default values of parameters in the Transmission parameter set 1
    Note that depending on parameter settings in transmission parameter set 1, the size of transmission parameter set 2, i.e. DCI size, may vary.
  Transmission parameter set 2: parameters indicated by physical layer (e.g. NR PDCCH channel)
    E.g. resource allocation, MCS, MIMO transmission scheme
  Note: some transmission parameter may belong to both set-1 and set-2
  Detail parameters and usage condition are TBD