## Slide 1: WF on Unified Codebook Structure for Type I and II CSI
Samsung, Intel, CATT, AT&T
R1-1613677
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th - 18th November 2016
Agenda item: 7.1.3.3

## Slide 2: Background: RAN1#86b
Agreement:
NR supports CSI reporting with two types of spatial information feedback
  Type I feedback: Normal
    Codebook-based PMI feedback with normal spatial resolution
  Type II feedback: Enhanced
    “Explicit” feedback and/or codebook-based feedback with higher spatial resolution
For Type I and II, CSI feedback per subband as well as wideband feedback are supported
For Type I and II, beam-related feedback can be included

## Slide 3: Proposal
Common/Unified NR codebook structure is used for both Type I and II.
  FFS NR codebook structure can be W1W2 or W1W2W3
  FFS on details on Type I and Type II, Type I can be implicit and Type II can be explicit and/or implicit (down selection between explicit and implicit will be done next meeting)
W1 codebook supports multiple types of vector groups
  Used for WB CSI reporting
  A UE is configured with a W1 codebook
  L ≥ 1 vectors can be selected from the W1 vector groups
Study the following for Type I and II CSI
  Type I: single vector selection and multiple vector combination
  Type II: explicit feedback based on multiple vector combination
    Examples of explicit feedback: channel, eigenvector, covariance matrix
    Study the following quantization alternatives:
      Magnitude and phase
      Real and imaginary
      Vector quantization