## Slide 1: WF on P-UE resource selection in partial sensing
Huawei, HiSilicon, NTT DOCOMO
3GPP TSG RAN WG1 Meeting #87
Reno, US 14th - 18th November 2016
Agenda item: 6.2.1.2.2
R1-1613693

## Slide 2: Background
In RAN1#86, the following were agreed for P-UE
  V2V sensing-based resource selection is the baseline; strive to define P-UE partial sensing-based resource selection to be as similar as possible to V2V sensing-based resource selection
In RAN1#86, the following were agreed for V-UE
    If the number of remaining resource after Step 2 is smaller than 20% of the total resources within the selection window, the UE repeats Step 2 using all the thresholds increased by 3 dB until the number of remaining resource after Step 2 is larger than 20% of the total resources.

## Slide 3: Background
  Similarly to what happens for V2V, it is possible that after sensing and resource exclusion, there are not enough remaining resources for resource selection.
  When P-UEs apply the threshold-increasing process using for V-UE, it could lead to unnecessary performance degradation for V(P)-UEs sharing this pool
  For instance, it is possible that there are plenty of available free resources outside of the sensed subframes

## Slide 4: Proposal
If a P-UE cannot find enough resources after SA decoding and PSSCH-RSRP based resource exclusion with the initial PSSCH-RSRP threshold
  PUE retriggers resource reselection with a different subset of sensing and selection subframes
  For the current transmission
    P-UE reuses the original selected resource if the resource exists and can accommodate the current transmission
    Otherwise random resource selection is used in resource pool allowing random selection
      The resources marked as reserved in the SA and determined as occupied after PSSCH-RSRP measurement should be excluded if it is included in the random resource pool