## Slide 1: WF on Discovery Enhancements for UEs with 1 PRB Bandwidth Limitation
Intel, Apple, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #90 R1-1714852
Prague, Czech Republic, 21st – 25th August 2017
Agenda item - 5.2.9.3

## Slide 2: Background
Physical structure of R12/13 PSDCH is based on 2 PRBs
R12/R13 discovery structure cannot be used by UEs with 1 PRB bandwidth limitation
Discovery enhancements are needed for UEs with 1 PRB bandwidth limitation

## Slide 3: Proposal
Capture in TR 36.746 that the following discovery design options are identified for UEs with 1 PRB BW limitation
  Option 1: Define 1 PRB / 1 TTI physical structure and reduce payload size
  Option 2: Define 1 PRB / 2 TTIs physical structure and keep the same payload size
  Option 3: Define 1 PRB / 1 TTI physical structure and increase modulation order (e.g. to 16-QAM)
From RAN1 perspective, all options are feasible. Option 2 and 3 can be supported without change of discovery message size and thus have lower impact on other WGs
Specific design options can be down-selected in the normative phase