## Slide 1: WF on solving coderate issue for supporting 64QAM in Rel-15 V2X
Huawei, HiSilicon, Qualcomm Incorporated, LG Electronics
3GPP TSG RAN WG1 Meeting #90 R1-1715086
Prague, Czech Republic, August 21-25, 2017
Agenda item – 5.2.3.2

## Slide 2: Background
For Rel-15 V2X UE supporting 64QAM
  effective code rate exceeds 0.931 for MCS18, MCS19, MCS20 for 16QAM
  effective code rate exceeds 0.931 for MCS24 through MCS28 for 64QAM

## Slide 3: Background
Similar issue occurs in LAA and was addressed by changing MCS switching point
  UEs assigned to transmit PDSCH in the 1nd slot of a subframe uses Modulation Order
  UEs assigned to transmit PDSCH in the 2nd slot of a subframe uses Modulation Order
MCS Index | Modulation Order | Modulation Order | TBS Index
0 | 2 | 2 | 0
1 | 2 | 2 | 1
2 | 2 | 2 | 2
3 | 2 | 2 | 3
4 | 2 | 2 | 4
5 | 2 | 4 | 5
6 | 2 | 4 | 6
7 | 2 | 4 | 7
8 | 2 | 4 | 8
9 | 2 | 4 | 9
10 | 4 | 6 | 9
11 | 4 | 6 | 10
12 | 4 | 6 | 11
13 | 4 | 6 | 12
14 | 4 | 6 | 13
15 | 4 | 6 | 14
16 | 4 | 6 | 15
17 | 6 | 6 | 15
18 | 6 | 6 | 16
19 | 6 | 6 | 17
20 | 6 | 6 | 18
21 | 6 | 6 | 19
22 | 6 | 6 | 20
23 | 6 | 6 | 21
24 | 6 | 6 | 22
25 | 6 | 6 | 23
26 | 6 | 6 | 24
27 | 6 | 6 | 25
28 | 6 | 6 | 26/26A
29 | 2 | 2 | Reserved
30 | 4 | 4 | 
31 | 6 | 6 | 

## Slide 4: Proposal
Introduce a modified MCS table for Rel-15 V2X UE
  The switching point from 16QAM to 64QAM is changed from MCS21 to MCS18

## Slide 5: Illustration
MCS Index | Modulation Order | TBS Index
0 | 2 | 0
1 | 2 | 1
2 | 2 | 2
3 | 2 | 3
4 | 2 | 4
5 | 2 | 5
6 | 2 | 6
7 | 2 | 7
8 | 2 | 8
9 | 2 | 9
10 | 2 | 10
11 | 4 | 10
12 | 4 | 11
13 | 4 | 12
14 | 4 | 13
15 | 4 | 14
16 | 4 | 15
17 | 4 | 16
18 | 4 6 | 17 16
19 | 4 6 | 18 17
20 | 4 6 | 19 18
21 | 6 | 19
22 | 6 | 20
23 | 6 | 21
24 | 6 | 22
25 | 6 | 23
26 | 6 | 24
27 | 6 | 25
28 | 6 | 26