## Slide 1: WF on Type 0 RA
NEC, …
3GPP TSG-RAN WG1 Meeting #90
Prague, Czech Republic, 21st – 25th August 2017
Agenda item 6.1.3.3.1.1
R1-1715099

## Slide 2: Background
LTE supports DL Type 0 and Type 1 where Type 0 has RBG level/coarser granularity and Type 1 has PRB level/finer granularity.
In practice, the coarser granularity provides a low overhead signalling of the RA scheme for larger allocations, while the finer granularity provides scheduling flexibility as well as to fill dis-continuous holes or left over resources.
The issue is that DL LTE Type 0 and Type 1 are treated in two different RA schemes. So, for NR, it would be beneficial to merge the benefits of DL Type 0 and Type 1 into a single resource allocation scheme.

## Slide 3: Background
Agreements:
For PDSCH/PUSCH, the RBG size/number can be changed along with the change of the BWP used for resource allocation.
FFS: If one or multiple of following option(s) is/are also used for RBG size/number determination:
  Opt. 1: Semi-statically configured size of Type0 RA bitmap
    Number and size of RBGs for a RA is determined based on size of BWP and the size of the bitmap.
  Opt. 2: Semi-statically configured RBG size(s) per BWP for deriving number of RBGs
    Number of RBGs in the BWP is determined by size of the BWP and the configured/indicated RBG size(s).
    FFS: Dynamic switching of RBG size(s).
  Opt. 3: DCI format/DCI format size (e.g. a compact DCI may be with a larger RBG size than a normal DCI).
  Opt. 4: Transmission durations (e.g. a shorter-duration transmission may be with a larger RBG size than a longer one).
  Opt. 5: RBG size is determined depending on the size of the BWP.
  Other options are not precluded.

## Slide 4: Proposals:
For a resource allocation scheme based on LTE DL RA type 0, for slot-based scheduling,
  The RBG size (P) is at least a function of the number of PRBs within the BWP.
  Dynamic switching between the RBG size (P) and RBG size = 1 is supported while keeping the RA overhead the same.
    RBG size = 1 covers only a portion of the bandwidth part.
  The number of bits for the RA field in the DCI in the BWP is given by
  where X is stands for D and U (downlink and uplink respectively)
    FFS: details of the header.

## Slide 5: Example:
potion 4
portion 3
portion 2
portion 1
Time
Freq
PDSCH
PDSCH
PDSCH
PDSCH
slot
Time
Freq
slot
PDSCH
RBG level granularity to cover the whole
bandwidth part, for example a bandwidth part of 100RBs using RBG size = 4.
PRB level granularity to cover a portion of the bandwidth part, for example a portion of 25RBs (100/4).