## Slide 1: R2-164380 “Way forward” for further mobility enhancements in LTE Intel, Ericsson, Nokia, Qualcomm, CATT

## Slide 2: Current options characteristics
Simultaneous Tx or Rx requiring 2 UE protocol stacks (Cat C & D)
UE indication to stop source eNB data transmission (option 6)
When the UE detach from source eNB: between start of the RF tuning phase until RRC Reconfiguration complete message to target (Cat A & B)
Combined RACH-less and make before break (option 4)

## Slide 3: Lessons learnt from Hetnet mobility WI
Most of the HOFs are due to the failure in HO command reception at the UE
  this implies the channel condition is poor during or after the HO command, UE is unlikely to receive UL grant from the source eNB
Most of the HOFs happen in handover from macro to small cell

## Slide 4: Discussions for down selection
Depending on pain vs gain, WI target should be to minimize the interruption time but not necessarily to zero interruption time
Cat C & D requires dual protocol stacks at the UE what indicates very high UE complexity
  Suggest not to consider these two Categories in this WI (they can be considered e.g. in NR)
From the lessons learnt in Hetnet mobility WI, the “UE indication” is unlikely to be delivered successfully.
  Suggest not to consider “UE indication” in this WI
  FFS if other mechanism to stop source eNB data transmission can be considered or it can be left up to the NW implementation
If RACH-less solution is not feasible in all scenarios (depending on the feedback from other WGs), this solution can be considered for handover to small cell and intra-eNB handover
Next step could be to down select options within Cat A and B