## Slide 1: Summary of RAN3 status on CU-DU split Option 2 and Option 3, and questions/issues for RAN2
RAN3 NR Rapporteur (NTT DOCOMO, INC.)
3GPP TSG RAN WG2 Meeting NR AdHoc
Spokane, Washington, USA, 17th-19th January 2017
Agenda Item: 3.4
Document for: Discussion
R2-1700637

## Slide 2: Introduction
Quote from RAN2/3 chairmen announcement of joint session
  Joint session on the topic of CU-DU (split Option 2vs3)
    RAN2 to present current status of NR UP stack
    RAN3 to prepare questions/issues for joint discussion with RAN2
    Aim for RAN2 to provide necessary information to assist RAN3 to take a decision on down selection between option 2 and 3, if possible
This document covers the 2nd point above (RAN3 to prepare …) and includes the following:
  Description of CU-DU split Option 2 and Option 3 based on the NR UP stack (which tries to take into account the latest RAN2 status), with highlight on possible impacts that they have on the NR UP stack
  Benefits and drawbacks of Option 2 and Option 3 discussed in RAN3, with highlight on the points where RAN3 would like to request RAN2 confirmation/feedback
2

## Slide 3: Description of Option 2 (PDCP/RLC split)
Description
In this option split option, RRC, PDCP are in the central unit. RLC, MAC, physical layer and RF are in the distributed unit.
3

## Slide 4: Description of Option 2 (PDCP/RLC split)
DU
CU
4
Overall layer 2 structure for NR (RAN2 agreement)
Layer 2 structure split into CU and DU (Option 2)

## Slide 5: Possible impact on NR UP stack with Option 2
None?
5

## Slide 6: Description of Option 3 (High RLC/Low RLC split)
Description
Low RLC may be composed of segmentation function
High RLC may be composed of ARQ and other RLC function
This option splits the RLC sublayer into High RLC and Low RLC sublayers such that for RLC Acknowledged Mode operation, all RLC functions may be performed at the High RLC sublayer residing in the central unit, while the segmentation maybe performed at the Low RLC sublayer residing in the distributed unit. Here High RLC segments RLC PDU based on the status reports, while Low RLC segments RLC PDU into the available MAC PDU resources
6

## Slide 7: Description of Option 3 (High RLC/Low RLC split)
DU
CU
7
Segmentation (Low RLC)
Only for RLC retx
using SO based resegment
For both RLC 1st tx and retx using SO based (re)segment
Overall layer 2 structure for NR (RAN2 agreement)
Layer 2 structure split into CU and DU (Option 3)

## Slide 8: Possible impact on NR UP stack with Option 3
The following is assumed for Option 3
  For initial RLC transmission,
    High RLC does not perform any segmentation, i.e. “1 RLC PDU = 1 RLC SDU + SN”
    These RLC PDUs are passed down from CU to DU
      These RLC PDUs are also buffered at the CU for possible RLC retransmission
    Low RLC at the DU can segment these RLC PDUs (using SO based segmentation) into the available MAC PDU resources
  For RLC retransmission
    High RLC can segment the RLC PDU (using SO based segmentation) to only pass down missing segments to the DU
RAN3 asks RAN2 to provide feedback on whether and (if so) how the above assumption would impact RAN2 discussion
8

## Slide 9: Benefits and drawbacks of Option 2
Benefit
  This option will allow traffic aggregation from NR and E-UTRA transmission points to be centralized. Additionally, it can facilitate the management of traffic load between NR and E-UTRA transmission points.
  Fundamentals for achieving a PDCP-RLC split have already been standardized for LTE Dual Connectivity, alternative 3C. Therefore this split option should be the most straight forward option to standardize and the incremental effort required to standardize it should be relatively small. [Further study needed for C-plane]
  The alignment between LTE-NR tight interworking and functional split may be beneficial at least in user-plane, considering migration
No particular questions from RAN3 to RAN2
9

## Slide 10: Benefits and drawbacks of Option 3
Benefit
  This option will allow traffic aggregation from NR and E-UTRA transmission points to be centralized. Additionally, it can facilitate the management of traffic load between NR and E-UTRA transmission points.
  This option may have the advantage of being more robust under non-ideal transport conditions because the ARQ and packet ordering is performed at the central unit.
  This split option may also have better flow control across the split.
  Centralization gains: ARQ located in the CU may provide centralization or pooling gains.
  The failure over transport network may also be recovered using the end-to-end ARQ mechanism at CU. This may provide protection for critical data and C-plane signaling.
  DUs without functions of RLC may handle more connected mode UEs as there is no RLC state information stored and hence no need for UE context.
  It may reduce processing and buffer requirements in DU due to absence of ARQ protocol.
  Could be used over multiple radio legs of different DUs for higher reliability (U-Plane and C-Plane). [Pending to multiple connectivity]
  This option may provide an efficient way for implementing intra-gNB RAN-based mobility.
  This option may provide an efficient means for implementing integrated access and backhaul to support self-backhauled NR TRPs.
Drawback
  Comparatively, the split is more latency sensitive than the split with ARQ in DU, since re-transmissions are susceptible to transport network latency over a split transport network.
RAN3 requests RAN2 feedback on whether Benefit #2, #7 to #9 and Drawback #1 are confirmed and what are their significance
10