## Slide 1: Way Forward on Inter frequency search requirements for configured frequencies without compressed mode
Qualcomm Incorporated

## Slide 2: Agreements
RAN4 is going to introduce RRM requirements for:
  A multi-carrier HSDPA UE (without Rel-8/9/10 optional searchers) able to have measurements for cell(s) on configured inter frequencies without requiring compressed mode regardless of activation/deactivation status of configured inter frequencies
  Configured frequencies could be either in single band or in dual bands.
  Multi-carrier HSDPA includes DC-HSDPA, DB-DC-HSDPA, 4C-HSDPA, NC-4C-HSDPA and 8C-HSDPA.
  UE requirements on the minimum number of inter frequencies to be monitored will be the same as for measurements with compressed mode.

## Slide 3: Way Forward
RAN4 will further discuss the following points
  Whether to introduce requirements independent of activation/deactivation status of configured inter frequencies
  Requirements for configured and activated inter frequencies
  Requirements for configured and deactivated inter frequencies
  Glitch requirements in the case of measurements for configured and deactivated inter frequencies