## Slide 1: WF on AWS extension operating band (Band 66)
Ericsson, Qualcomm, Verizon, T-Mobile USA, US Cellular, Bell Mobility, AT&T, Intel
R4-158425

## Slide 2: Background
Band 66 is specified as 1710-1780/2110-2200MHz
The DL frequencies 2180-2200MHz are to be used in CA operation since there is no associated UL
A Band 66 UE which is non-CA capable can cover the frequencies 2180-2200MHz from a hardware perspective (i.e. DL filter)
At RAN4#76bis, it was agreed to require CA capable UEs that support Band 66 to support intra-band CA to meet interoperability
At RAN4#77, it has been discussed to require non-CA capable UEs to support the entire Band 66 in order to avoid market fragmentation and in the spirit of interoperability

## Slide 3: WF on Band 66
A note is included outside the Operating bands table of TS 36.101 stating
  NOTE: A UE that supports Band 66 should support the entire DL operating band
Non-CA capable devices do not test support for the frequency 2180-2200MHz