## Slide 1
3GPP TSG-RAN WG4 #78
ST. Julian, Malta, 15 – 19 Feb, 2016
Agenda item: 8.13.1
LG Electronics
WF on adjacent channel coexistence scenarios for V2V
R4-161408

## Slide 2: Objective
Define adjacent channel coexistence evaluations assumptions and methodology for licensed/unlicensed bands V2V Services during 4 meeting times in RAN WG4 to derive ACLR. (restricted time limit to complete V2V Core requirements)
1) Licensed band (2GHz)
Consider following interference scenarios
  V2V-to-LTE
  LTE-to-V2V
  Both scenarios would be analyzed
  Reuse D2D deployment simulation parameters
2) Unlicensed band (5.9GHz)
Consider following interference scenarios
  V2V-to-Wifi/LAA/DSRC
  Wifi/LAA/DSRC-to-V2V
  1st priority is V2V-to-LAA and LAA-to-V2V scenario
  2nd priority is V2V-to-DSRC scenario (if discussion time is available in WI)
  Reuse LAA deployment simulation parameters (RAN4 only consider DL transmission for LAA)

## Slide 3: 1st Scenarios in Licensed band (2GHz)
Case 1 (Aggressor-Victim)
  V2V UE-to-LTE BS
Case 2 (Aggressor-Victim)
  LTE UE-to-V2V UE
  Consider V2V based on PC5 operation in licensed bands
  Reuse D2D deployment simulation parameters
LTE
V2V
f
V2V
LTE
f

## Slide 4: 2nd Scenarios in Unlicensed band (5.9GHz)
Case 3 (Aggressor-Victim)
  V2V UE-to-LAA UE
Case 4 (Aggressor-Victim)
  LAA BS-to-V2V UE
Case 5 (Aggressor-Victim): Optional
  V2V UE-to-DSRC UE
    Interesting Vendors provide adjacent coexistence simulation results
  Reuse LAA deployment simulation parameters.
LAA
V2V
f
V2V
LAA
f
V2V
DSRC
f

## Slide 5: Evaluation methodology
Static simulations
  Monte-carlo based static simulations.
Evaluation metric
  Legacy system Throughput degradation due to adjacent channel interferer(s)
  Need further discussion on evaluation metric for the V2V victim scenarios.
    Encourage vendors to provide their view on this since RAN1 has ongoing discussion on the detail of the parameters (e.g. RB allocation and RS design)

## Slide 6: Way Forward
Coexistence scenarios to derive ACLR/ACS
  1st Scenario (Aggressor-Victim) in licensed band
    V2V UE-to-LTE BS
    LTE-UE-to-V2V UE
  2nd Scenario (Aggressor-Victim) in unlicensed band
    V2V UE-to-LAA UE
    LAA BS-to-V2V UE
    V2V UE-to-DSRC UE (optional)