## Slide 1: Way forward on UE transmit timing requirements in NB-IoT
Ericsson, Nokia
3GPP TSG-RAN WG4 Meeting #78bis R4-162866
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Background
Analysis on feasibility of NB-IoT inheriting E-UTRAN legacy behavior for UE autonomous UL transmit timing updates and application of TAC is provided in R4-161945.
NB-IoT devices operate in half-duplex mode and use repetitions of transmissions to facilitate extreme coverage enhancements.
Base station implementation uses message accumulation and soft combining to receive and decode messages transmitted by devices operating in enhanced coverage.
Timing adjustments during the accumulation phase introduces linear phase on the base station receiver side, and thereby degrades the accumulated signal.

## Slide 3: Working assumptions
Onset of a new UL repetition period shall be considered to be an initial transmission.
UE autonomous UL timing updates are not allowed during UL repetition periods.

## Slide 4: Agreement
For the RAN4 NB-IoT AH in May, interested companies are to provide:
Analyses on the feasibility of the working assumptions (1-2).
Analyses on the time needed to detect a change in downlink timing given the use of DL repetitions.
Analyses on feasibility of specifying timing error requirements based on a 1.92MHz timing resolution, although the UE implementation may use a lower sample rate.
Analyses on whether relaxations compared to timing error requirements for legacy UE in 1.4MHz cell are needed.
Other analyses relating to UL timing error are not precluded.