## Slide 1: Way forward on additional channel model for bidirectional SFN scenario
Huawei,HiSilicon, Intel, MediaTek Inc.,
NTT DOCOMO, INC, CMCC, ITRI,Qualcomm,Samsung,Ericsson,CATT
3GPP TSG-RAN WG4 Meeting #78bis R4-163052
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Background
In #78 meeting, the agreements on scenario assumption is:
  Scenarios assumptions
    Simulation assumptions agreed in SI are treated as baseline, and others assumptions are not precluded.
      Following parameters are encouraged for evaluation.
Parameter | Value | 
 | SFN scenario 1 | SFN scenario 2d
RRH Railway track distance (Dmin) | 300m | 5m
Distance between RRH (Ds) | 1km; 1.5km | 500m
Cell ISD | 2km (2RRHs connect to 1 BBU); 3km (2RRHs connect to 1 BBU) Other number of RRH is not precluded | 1km (2RRHs connect to 1 BBU);
RRH height (compared to railway track) | 25m | 2.5m

## Slide 3: Options of channel model for SFN scenario
There are 5 additional channel models proposed for bidirectional SFN scenario in RAN4#78bis other than the agreed baseline assumption,
  Option 1: captured in R4-162016 (4 taps) baseline
  Option 2: captured in R4-161950 (4 taps)
  Option 3: captured in R4-162468 (3 taps)
  Option 4: captured in R4-162721 (3 taps)
  Option 5: captured in R4-161632 (4 taps)
Down selection is needed for channel model of SFN scenario with more than 2-path.
Option 1(R4-162016) from Huawei as baseline.

## Slide 4: Baseline
Option 1: R4-162016,huawei (baseline)
Note: companies are encouraged to provide the simulation results for scenario 1 and 2d in slide8 based on the baseline channel model

## Slide 5: SFN deployment for the scenario
The channel model is derived based on the SFN deployment in the following Figure 1.
There are four RRHs with the same Cell ID for simplicity.
Figure 1: Deployment of SFN

## Slide 6: Assumption
Four RRHs with the same Cell ID are assumed for simplicity. The four stations are located at
  Scenario 1
    x1 = (0+j300) meter
    x2=(1000+j300)meter
    x3= (2000+j300)meter
    x4=(3000+j300)meter
  Scenario 2d
    x1 = (0+j5) meter
    x2=(500+j5)meter
    x3= (1000+j5)meter
    x4=(1500+j5)meter
The train location is denoted as
    y=a+j*0 and a~[0,+inf], which means the train is right on the track.
And the height of the station was neglected for simplicity.

## Slide 7: Equations for the channel model
The power level for the signal from kth BS:
The Doppler shift for the signal from kth BS:
The relative delay for the signal from kth BS:
v is the moving speed of the train, is the center frequency, and C is the velocity of light.

## Slide 8: Parameters for SFN scenario
Parameter | Value
 | 1000 m
 | 300m
 | 350 km/h
 | 875 Hz
Table 1 Parameters for SFN scenario 1
Parameter | Value
 | 500 m
 | 5 m
 | 350 km/h
 | 875 Hz
Table 2 Parameters for SFN scenario 2d

## Slide 9: Curve of normalize relative power
According the equation for the channel model and the parameters for SFN scenario, the normalized power, Doppler shifts , relative delay is shown in figure 1~3,
Figure 1 Normalized power level in scenario 1
Note: In Figure 1~3, the parameters in table 1 are used as an example.

## Slide 10: Curve of Doppler shifts
Figure 2 Doppler shifts in scenario 1

## Slide 11: Curve of relative delay
Figure 3 Relative delay in scenario 1

## Slide 12: For information
For the evaluation, we can evaluate the performance of scenario 1 from location (along the track) at
  Option 1: 500 meters to 2500 meters
  Option 2: 1000 meters to 2000 meters
and scenario 2d from location (along the track) at
  Option 1: 250 meters to 1250 meters
  Option 2: 500 meters to 1000 meters