## Slide 1: On EVM evaluation for multi-numerology multiplexing
Agenda item: 10.4.1.2
Document for: Discussion
Source: Orange
R4-1701763
3GPP TSG-RAN WG4 Meeting #82
Athens, Greece, 13 - 17 February, 2017

## Slide 2: Summary of the issues to study
This contribution studies the EVM with filtering/windowing for multiplexed numerologies case.
different multiplexing cases are evaluated, e.g.
15 KHz
30 KHz
15 KHz
30 KHz
30 KHz
one-side
two-side
GB
GB
GB

## Slide 3: Evaluation assumptions
Waveform candidates
  f-OFDM [1]: filter length 50% of symbol length
  WOLA [2]: window length 2% of symbol length at Tx side only
  FC-OFDM [3]: window length 144 for 15KHz SCS and 72 for 30 KHz SCS
PA model: Rapp model with 11.6 dB back-off
Two numerologies case: 15 KHz (target), 30 KHz (interference)
10 PRBs for target and interference allocations, individually
Guard band: 1 PRB based on 15 KHz SCS
Spectral efficiency estimation is based on theoretical Shannon capacity
[1] R1-165425, f-OFDM scheme and filter design, Huawei, HiSilicon
[2] R1-162199, Waveform candidates, Qualcomm Inc.
[3] R1-1610404, FC-OFDM discussion based on RAN1#86 waveform agreements, Orange

## Slide 4: One-side multiplexed numerologies
Observations
  Without Rx window/filter, WOLA and f-OFDM have similar level of interference resistance
  WOLA with only Rx filtering provides better SE than f-OFDM with Rx filtering
  WOLA with only Rx filtering attains the same SE as the one using optimized spectral confined waveform

## Slide 5: two-side multiplexed numerologies
Observations
  without Rx window/filter, WOLA and f-OFDM have similar performance
  with same Rx filtering, WOLA and f-OFDM have similar performance

## Slide 6: Observations
Without Rx filtering, WOLA and f-OFDM have similar performance for both one-side and two-side numerologies multiplexing
Filtering on Tx side seems not necessary
In downlink, Tx filtering complicates processing in the case of distributed service-band multiplexing, such as
WOLA and f-OFDM with Rx filtering yield similar spectral efficiency
eMBB
URLLC
eMTC
eMTC