## Slide 1: WF on NR spectrum utilization
Huawei, HiSilicon,…
3GPP TSG RAN WG4 Meeting #82
Athens, Greece, 13th - 17th February 2017
Agenda: 10.4.1.1
R4-1702033

## Slide 2: Background
In RAN4 #80bis [1], it was agreed that
  Carrier spectrum utilization, denoted by Y, is assumed to be higher than 90% in RAN4 future study and RAN4 requirements should be defined based on this assumption.
    Y may depend on specific numerology and carrier bandwidth. It is FFS how the guard band at the edge of a channel should be defined when different numerologies are frequency multiplied
    Y may depend on the BS/UE implementation complexity and declared capability. It is possible to define different value of Y for different BS/UE capabilities with compliance of related RF requirements, e.g. EVM, ACLR, SEM, etc. It is important to verify both the spectrum and EVM results at the same time in order to ensure well performing and robust system
Companies’ evaluation results show that Y varies with numerology, carrier bandwidth and spectrally confinement techniques (filtering/windowing, also their length).

## Slide 3: WF
Spectrum utilization for each carrier bandwidth is only specified for single numerology.
For FDMed mixed numerologies in a carrier, it is proposed that NR doesn’t define the spectrum utilization in an explicit way, but leave it as an implementation issue
  The guard band at each edge of the carrier is determined based on the spectrum utilization corresponding to the numerology at carrier bandwidth edge
  The guard band between two numerologies is not explicitly specified, i.e. left as an implementation issue
    FFS how to decide the guard band size for defining in-band requirements

## Slide 4: WF
To strive for high spectrum utilization while allowing the flexibility in implementation, it is proposed to define NR spectrum utilization as a set of different values, corresponding to different BS capabilities and UE capabilities ( >= 90%) , taking into account different numerology, carrier bandwidth, and applied waveform with different parameters.
  The detailed values within the set is FSS (e.g. [A%, B%, C%])
  The values correspond to minimum, medium, and high spectrum utilization level