## Slide 1: Way forward on emissions scaling
Agenda Item: 7.13.3.1
Document for: Approval
Source: Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 #82 R4-1702266
Athens, Greece, 13th – 17th February 2017

## Slide 2: Background
During the AAS evening ad hoc meeting, contributions on emissions scaling [1][2] were discussed
As there is no conducted interface and hence no TAB connectors in the OTA AAS BS architecture, the contributions identified and discussed the following open issues:
  NTXU,counted is fixed or adapt REL-13 NTXU,counted for OTA requirements
  REL-13 AAS scaling terminology is defined in terms of TAB connectors

## Slide 3: Background
The current scaling factor NTXU, counted is calculated from a number of defined and declared parameters, of these 3 of them have been identified as referring to the conducted interface or the TAB connectors.
active transmitter unit: transmitter unit which is ON, and has the ability to send modulated data streams that are parallel and distinct to those sent from other transmitter units to one or more TAB connectors at the transceiver array boundary
Ncells A declared number corresponding to the minimum number of cells that can be transmitted by an AAS BS in a particular band with transmission on all TAB connectors supporting the operating band.
TAB connector TX min cell group: operating band specific declared group of TAB connectors to which TX requirements are applied.
NOTE: Within this definition, the group corresponds to the group of TAB connectors which are responsible for transmitting a cell when the AAS BS setting corresponding to the declared minimum number of cells with transmission on all TAB connectors supporting an operating band, but its existence is not limited to that condition.
In order to make the scaling factor suitable for the all OTA requirements these definitions must be made suitable for the OTA AAS BS architecture [3] and not refer to TAB connectors or the conducted interface.

## Slide 4: Way forward
Companies are encouraged to submit proposals for the next meeting addressing the following open issues:
  For OTA unwanted emissions requirements, two options are possible:
    a. Use different scaling factor for hybrid and OTA requirements, for OTA use a fixed scaling factor [NTXU,xxx] where [NTXU,xxx]=8 for E-UTRA or 4 for UTRA. The final name for NTXU,xxx is FFS.
    b. Use the same scaling factor for both hybrid and OTA requirements (NTXU,counted ) using the same scaling concept as in REL-13 AAS but with minor modifications as suggested in the next slide

## Slide 5: Way Forward
For option b, the proposed modifications are as follows:
  the definitions can be modified in such a way to maintain the correct meaning and be applicable to both the hybrid AAS BS architecture and the OTA AAS BS architecture:
    active transmitter unit: transmitter unit which is ON, and has the ability to send modulated data streams that are parallel and distinct to those sent from other transmitter units to be radiated in the far field.
    Ncells A declared number corresponding to the minimum number of cells that can be transmitted by an AAS BS in a particular band with transmission on all Transceiver units supporting the operating band.
    TAB connector TX min cell group: operating band specific declared group of Transceiver units to which TX requirements are applied.
    NOTE: Within this definition, the group corresponds to the group of Transceiver units which are responsible for transmitting a cell when the AAS BS setting corresponding to the declared minimum number of cells with transmission on all Transceiver units supporting an operating band, but its existence is not limited to that condition.
Other forms of wording are not precluded.

## Slide 6: References
[1] R4-1701861 , OTA unwanted emission requirements, Nokia, Alcatel-Lucent Shanghai Bell
[2] R4-1701726 , Emissions scaling, Huawei
[3] R4-1701730 TP to TR37.843 Updating reference architecture diagrams Huawei