## Slide 1: WF on simulation assumptions for feNB-IoT Measurement Accuracy
Nokia, Nokia Shanghai Bell
R4-1708338
3GPP TSG-RAN WG4 #84
Berlin, Germany, 21 – 25 August, 2017
Agenda Item: 8.24.3

## Slide 2: Simulation parameters
Parameters | Value | Comments
Measurement bandwidth | 1 resource block | Both RSRP and RSRQ measured over 1 RB*
L1 measurement period | Normal mode: 200ms, 400ms (800ms) Extended mode: 400, 800ms (1600 ms) | 
Measurement sampling rate | 40ms | 
Sample duration (NRS occasions) | In-band: 1ms (1), 5ms (2), 11ms (3), 21ms (6) | Need to account NSSS signal.
L3 filtering | Disabled | 
Antenna configuration | In-band: 2 Tx, 1 Rx | 
Channel model | AWGN, EPA 1Hz, ETU 1Hz | 
Measurement type | NRS only based | 
CP length | Normal | 
Carrier frequency | 2.0 GHz | 
Ec/IoT | Normal mode: -6 dB Extended mode: -15 dB | AWGN noise
Frequency error modeling | ±50 Hz | With respect to reference cell
*NOTE: RSRQ is be based on using all symbols in the measured subframe |  | 

## Slide 3: Way forward
Companies are encouraged to provide for next meeting:
  Initial simulation results for NRSRP accuracy
  Initial input on the L1 measurement period