## Slide 1: Way forward on the UE demodulation impact due to CRS muting
Ericsson
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 - 25, August, 2017
R4-1708701

## Slide 2: Background
RAN1 are going to introduce a capability signaling to mute CRS outside the BL UE narrowband/wideband, and have sent LS [R4-1704502] to RAN4 to ask the
  Minimum amount(s) of CRS
  Value(s) of X corresponding to number of PRBs outside the narrowband/wideband used by BL UEs for CRS.
The idea of the CRS muting in Rel-15 eFeMTC WI is to introduce a capability to make sure that BL UE uses the signal transmitted only within the UE maximum channel width.
If the eNB knows the BE UE has this capability then eNB can turn off the CRS transmission on RPBs which is not used by BL UEs. Therefore, RAN1 is asking the amount(s) of CRS the network can turn off.
RAN4#84 discussed the PDSCH performance impact due to CRS muting. Some companies think extra CRS on X PRB outside the narrowband/wideband and on Y subframe before/after the PDSCH transmission is beneficial to improve the PDSCH demodulation performance.

## Slide 3: Way forward
Companies are encouraged to bring the investigation results if Cat-M1/M2 UE can use CRS on X PRB(s) outside the narrowbands/wideband where PDSCH is transmitted.
Companies are also encouraged to bring the investigation results if Cat-M1/M2 UE use CRS on Y subframe(s) before/after the PDSCH transmission.

## Slide 4: Simulation assumption
[1] R4-1706202, “Way forward on FeMTC UE demodulation requirements”, Ericsson.
Parameters | Values
Test case | Cat-M1, TM2, CE Mode A, EPA5 (Test 1 in TS36.101 8.11.1.1.1) Cat-M1, TM6, CE Mode A, EPA5 (Test 2 in TS36.101 8.11.1.1.3) Cat-M1, TM2, CE Mode B, ETU1 (Test 1 in TS36.101 8.11.1.1.3) Cat-M2, TM2, CE Mode A, EPA5 ([1]) Cat-M2, TM2, CE Mode B, ETU1 ([1])
System bandwidth | 10MHz for Cat-M1, 20MHz for Cat-M2
X = (Number of PRBs outside the narrowband/wideband used for PDSCH/MPDCCH transmission) | 0 (No extra CRS outside narrowband/wideband) 1, 2, 3, 6 (other values are not precluded)
Y = (Number of subframes before and after the PDSCH transmission) | 0 (No extra CRS before/after the PDSCH transmission) 1 (other values are not precluded)

## Slide 5: Example of CRS muting for eFeMTC
Example of CRS transmission X=2 PRBs outside the narrowband used for PDSCH transmission and Y=1 subframe before/after the PDSCH transmission.