## Slide 1: WF on BS transmitter intermodulation for NR sub-6GHz
ZTE, []
3GPP TSG-RAN WG4-NR Meeting # 84
Berlin, Germany, 21 – 25 August, 2017
R4-1708871

## Slide 2: Agreements
In RAN4#84, BS transmitter intermodulation was discussed and the following proposal was agreed:
  Proposal : similar to LTE, for NR sub 6GHz, only “Co-location transmitter intermodulation” case should be defined for Range 1-C-N, and both “Co-location transmitter intermodulation” and “Intra-system transmitter intermodulation” cases for range 1-C-A.

## Slide 3: Way Forward
Co-location transmitter intermodulation case
  Considering the following principles to define interfering signal:
    Specify only one interfering signal type for all wanted NR signal
      FFS: interfering signal type (NR or LTE signal)
    Specify only one channel bandwidth for interfering signal by identifying the worst case where the interfering signal has the highest PSD assuming the same transmission power level:
      Choose 5MHz bandwidth if LTE signal is agreed
    Specify “Rated total output power in the operating band – 30 dB” for the interfering signal level

## Slide 4: Way forward (Cont’d)
Intra-system transmitter intermodulation case
  the way to define interfering signal in AAS could be reused for NR range 1-C-A.
    Specify NR signal of the same channel bandwidth as the wanted signal as interfering signal
    Power level declared by the base station manufacturer

## Slide 5: Way forward (Cont’d)
For NR range 1-O eAAS
    FFS: Whether or not only co-location transmitter intermodulation case is needed