## Slide 1
NR MPR simulation assumptions for sub-6 GHz operation
Nokia
R4-1708912

## Slide 2
Issues to be agreed
Purpose of this contribution is to agree simulation assumptions for NR sub-6 GHz operation. List of topics to be agreed is below.
PA calibration point
Tx Modulator impairments
ACLR MBW
Spectrum utilization (already agreed)
Sub-block alingment
MPR Table format
Earlier agreements from R4-1706980 WF on MPR evaluation assumption RAN4#NR2 are added into annex.

## Slide 3
References
REFERENCES
R4-1707071 MPR evaluation results for sub 6GHz Samsung
R4-1707395 MPR evaluations for Sub-6GHz Intel Corporation
R4-1707598 S6 Contiguous MPR and UE assumtions Nokia, Skyworks Solutions, Inc.
R4-1707702 Impact of ACLR Measurement BW and TRX Impairments on NR UE MPR Skyworks Solutions Inc.
R4-1707703 Preliminary NR Sub-6GHz UE AMPR Results for Bands Supporting UTRA Skyworks Solutions Inc.
R4-1708089 Initial MPR analysis results for sub-6GHz UE LG Electronics Inc.
R4-1708606 NR transmission bandwidth configuration for MPR evaluation Qualcomm Incorporated
R4-1708607 Initial MPR simulation results for Sub6 NR bands Qualcomm Incorporated
R4-1707601 DFT-s-OFDM Spectrum Utilization and TX BW Derived from Agreed NR SU Nokia, Skyworks Solutions, Inc.

## Slide 4
PA calibration point
Proposal 1 from [3]
PA calibration point: No MPR allowed for 100 RB QPSK DFT-s-OFDM (15KHz SCS) signal
Proposal 2 from [8]
The PA was calibrated to the conventional LTE reference i.e. 1 dB MPR for 100 RB QPSK DFT-s-OFDM (15KHz SCS) signal
MPR results may be provided with both PA calibration point proposals. Outcome of MPR evaluation is discussed in nexr RAN4 meeting and decisision is made concearning the PA calibration point

## Slide 5
Tx Modulator impairments
Based on AH discussion
• IQ suppression 28 dBc up to 6 GHz
• Carrier leakage 28 dBc up to 6 GHz
• CIM3 = FFS.

## Slide 6
ACLR MBW
ACLR is a ratio of power of wanted signal within maximum transmission bandwidth among the SCSs for a channel BW and power falling into victim system from the wanted signal within an available maximum transmission bandwidth among the SCSs for a channel BW.
Offset for the adjacent measurement BW centre is +/- Channel BW from wanted channel centre (in the middle of the Channel).
Table below provides these measurement BW in the last row.
Sub-6GHz | SCS [kHz] | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 |  | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
SU_CP-OFDM [#RB] | 15 | 25 | 52 | 79 | 106 | 133 | 216 | 270 | N.A | N.A | N.A
 | 30 | 11 | 24 | 38 | 51 | 65 | 106 | 133 | 162 | 217 | 273
 | 60 | N.A | 11 | 18 | 24 | 31 | 51 | 65 | 79 | 107 | 135
TXBW [MHz] | 15 | 4.5 | 9.36 | 14.22 | 19.08 | 23.94 | 38.88 | 48.6 | NA | NA | NA
 | 30 | 3.96 | 8.64 | 13.68 | 18.36 | 23.4 | 38.16 | 47.88 | 58.32 | 78.12 | 98.28
 | 60 | NA | 7.92 | 12.96 | 17.28 | 22.32 | 36.72 | 46.8 | 56.88 | 77.04 | 97.2
TXBWsym [MHz] | 15 | 4.515 | 9.375 | 14.235 | 19.095 | 23.955 | 38.895 | 48.615 | NA | NA | NA
 | 30 | 3.99 | 8.67 | 13.71 | 18.39 | 23.43 | 38.19 | 47.91 | 58.35 | 78.15 | 98.31
 | 60 | NA | 7.98 | 13.02 | 17.34 | 22.38 | 36.78 | 46.86 | 56.94 | 77.1 | 97.26
maxTXBW [MHz] | lowest | 4.515 | 9.375 | 14.235 | 19.095 | 23.955 | 38.895 | 48.615 | 58.35 | 78.15 | 98.31

## Slide 7
Spectrum utilization
SU are agreed in RAN4#84
SCS [kHz] | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
CP-OFDM full allocation based on agreed SU |  |  |  |  |  |  |  |  |  | 
15 | 25 | 52 | 79 | 106 | 133 | 216 | 270 | N.A | N.A | N.A
30 | 11 | 24 | 38 | 51 | 65 | 106 | 133 | 162 | 217 | 273
60 | N.A | 11 | 18 | 24 | 31 | 51 | 65 | 79 | 107 | 135
DFT-s-OFDM full allocation based on agreed SU - all positions within the CP-OFDM RB allocation are valid for full and partial allocations |  |  |  |  |  |  |  |  |  | 
15 | 25 | 50 | 75 | 100 | 128 | 216 | 270 | N.A | N.A | N.A
30 | 10 | 24 | 36 | 50 | 64 | 100 | 128 | 162 | 216 | 270
60 | N.A | 10 | 18 | 24 | 30 | 50 | 64 | 75 | 100 | 135
Proposal from [9]: DFT-s-OFDM RB allocation should satisfy following rules:
Maximum number of RB is the lowest number closest to the max CP-OFDM number of RB satisfying equation 1.
RBstart possibilities follow equation 2.
number of RB=2^X*3^Y*5^Z (equation 1)
RBstart DFT-s-OFDM range = 0 to (CP-OFDM maxRB)–(DFT-s-OFDM #RB) (equation 2)
Worst case positon of RB start 0 for DFT-s-OFDM RB allocation is used for MPR evaluation.

## Slide 8
Sub-block alingment
Proposal 1 from [7]
Sub-block alingment is dependent from channel raster but at least 100 khz raster will be specified for LTE refarming bands.
Offset of the center frequency of the transmission bandwidth configuration for worst case guard band (100 kHz channel raster).

## Slide 9
MPR Table format Proposal 1 from [4]
Edge allocation means that allocation starts from RB0 or ends to the highest RB at the higher edge of the allocation. MPR will be smaller than for full alocation
Partial allocation is smaller than full allocation
In channel allocation is a allocation which is not in the edge. The intention is to have cases when allocation is not SEM or ACLR limited and MPR is smaller than for edge allocation.
The TBD in the table means that a requirement will be developed in form of a number or an equation
AH conclusion: It is ok to use the proposed format for next step. Further fine tune can be applied after seeing the simulation results.
Waveform | Modulation | MPR [dB] for all channel bandwidths and SCS |  | 
 |  | Full allocation | Edge small partial allocation | In channel partial allocation
DFT-s-OFDM | Pi/2 BPSK* | TBD** | TBD** | TBD**
DFT-s-OFDM | QPSK | TBD | TBD** | TBD**
DFT-s-OFDM | 16QAM | TBD | TBD** | TBD**
DFT-s-OFDM | 64QAM | TBD | TBD** | TBD**
DFT-s-OFDM | 256QAM | TBD | TBD** | TBD**
CP-OFDM | QPSK | TBD | TBD | TBD
CP-OFDM | 16QAM | TBD | TBD | TBD
CP-OFDM | 64QAM | TBD | TBD | TBD
CP-OFDM | 256QAM | TBD | TBD | TBD

## Slide 10
Earlier agreements from R4-1706980 WF on MPR evaluation assumption RAN4#NR2 are added into annex in the next slides.

## Slide 11: Agreement
CBW, SCS, SU [R4-1706942]
RB allocation and RB numbering
Since there is different feasible RB allocation depending on SCS and types of waveforms, RB numbering may become confusing. In the case of this WF RB0 was chosen to be the left most RB of the minimum full RB allocation using CP-OFDM based on Spectrum Utilisation agreement.
Since DFT-s-OFDM does not support the same number of RB than CP-OFDM, for example a 100RB waveforms is shifted left by 3RB compared to a corresponding 106RB CP-OFDM case as this is illustrated in Figure 1 bellow.
For CP-OFDM number of RB will be aligned to the agreement for spectrum utilisation
For DFT-s-OFDM, number of RB for full allocation will be the closest to the CP-OFDM full allocation that satisfies number of RB=2^X*3^Y*5^Z

## Slide 12: Agreement
CBW, SCS, SU [R4-1706942]
  Sub6
    The below minimum set of evaluated waveform for calibration, which does not preclude evaluation of a bigger set.
Waveform type | Modulation order | Channel BW | SCS | RB allocation | remark
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 100RB3 | Maximum DFT-s-OFDM allocation
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 18RB0 | Channel edge (LTE 0dB MPR for QPSK)
DFT-s-OFDM | QPSK, 16QAM | 20MHz | 15kHz | 18RB18 | Inside channel
DFT-s-OFDM | QPSK, 16QAM | 100MHz | 30kHz | 270RB1 | Maximum channel BW
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 106RB0 | Allocation for spectrum utilisation
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 18RB0 | Channel Edge
CP-OFDM | QPSK, 16&64QAM | 20MHz | 15kHz | 18RB18 | Inside Channel
CP-OFDM | QPSK, 16&64QAM | 100MHz | 30kHz | 273RB0 | Allocation for spectrum utilisation & max CH BW
Companies are encouraged to report reduced MPR and negative MPR cases Companies are encouraged to report which criteria is limiting and when applicable which transmitter impairments drives the limitation Companies are encouraged to provide their view of Pi/2 BPSK use at sub-6GHz |  |  |  |  | 
    Results are similarly reported as positive or negative compared to agreed reference waveform maximum power in R4-1706944
    For transmitter impairment agreed values in R4-1706944 are used
    Reporting absolute output power is also acceptable.

## Slide 13: Agreement
Tx maximum output power
  Sub6
    Conducted power of both 23 dBm and 26 dBm

## Slide 14: Agreement
EVM
  Sub6
    For both DFT-s-OFDM, CP-OFDM [R4-1706612]
Modulation | EVM
Pi/2 BPSK | FFS%
QPSK | 17.5%
16QAM | 12.5%
64QAM | 8%
256QAM | 3.5%

## Slide 15: Agreement
In-band emissions
  Sub6 [R4-1706693]
    Apply LTE in-band emission requirement for NR Sub-6 GHz MPR studies as defined in TS 36.101 clause 6.5.2.3 until NR Sub-6 GHz in-band emission requirement is agreed.
    Use standard LTE UE assumptions for PA linearity, IQ-Image and LO leakage or Use UE assumptions as proposed in R4-1706690.
    Type and the details conditions of BB filter needs to be provided together with the simulation results as much as possible.

## Slide 16: Agreement
SEM
  Sub6 [R4-1706692]
ΔfOOB (MHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 100 MHz | Measurement bandwidth
± 0-1 | -15 | -18 | -20 | -21 | -22 | -24 | -24 | -24 | -24 | -24 | 30 kHz
± 1-5 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | -10 | 1 MHz
± 5-6 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 
± 6-10 | -25 |  |  |  |  |  |  |  |  |  | 
± 10-15 |  | -25 |  |  |  |  |  |  |  |  | 
± 15-20 |  |  | -25 |  |  |  |  |  |  |  | 
± 20-25 |  |  |  | -25 |  |  |  |  |  |  | 
± 25-30 |  |  |  |  | -25 |  |  |  |  |  | 
± 30-40 |  |  |  |  |  |  |  |  |  |  | 
± 40-45 |  |  |  |  |  | -25 |  |  |  |  | 
± 45-50 |  |  |  |  |  |  |  |  |  |  | 
± 55-60 |  |  |  |  |  |  | -25 |  |  |  | 
± 60-65 |  |  |  |  |  |  |  | -25 |  |  | 
± 65-80 |  |  |  |  |  |  |  |  |  |  | 
± 80-85 |  |  |  |  |  |  |  |  | -25 |  | 
± 85-100 |  |  |  |  |  |  |  |  |  |  | 
± 100-105 |  |  |  |  |  |  |  |  |  | -25 | 

## Slide 17: Agreement
ACLR
  Sub6
    PC3(23dBm) [R4-1706582]
      30 dBc for NR vs NR with the same channel bandwidths up to 100MHz
      If EUTRA CHBW = NR CHBW only the NR ACLR of 30 dBc shall be measured
      UTRA1=33 dBc, UTRA2=36 dBc
    PC2(26dBm) [R4-1706556]
      31 dBc for NR vs LTE and NR vs NR with the same channel bandwidths

## Slide 18: Agreement
Spurious emissions
  Sub6 [R4-1706551]
Frequency Range | Maximum Level | Measurement bandwidth | NOTE
9 kHz  f < 150 kHz | -36 dBm | 1 kHz | 
150 kHz  f < 30 MHz | -36 dBm | 10 kHz | 
30 MHz  f < 1000 MHz | -36 dBm | 100 kHz | 
1 GHz  f < 12.75 GHz | -30 dBm | 1 MHz | 
12.75 GHz ≤ f < 5th harmonic of the upper frequency edge of the UL operating band in GHz | -30 dBm | 1 MHz | 1
12.75 GHz < f < 26GHz | -30dBm | 1MHz | 2
NOTE 1: Applies for Band that the upper frequency edge of the UL Band more than [2.69] GHz NOTE 2: Applies for Band that the upper frequency edge of the UL Band more than [5.2] GHz |  |  | 

## Slide 19: Agreement
Other
  MRP for non-contiguous allocation [Meeting minute of R4-1706828]
    It is evaluated with the understanding that contiguous evaluation is prioritized over non-contiguous allocation. Higher allocation ratio for non-contiguous allocation is more interest.