## Slide 1: WF on NR RLM
Ericsson, …
3GPP TSG-RAN WG4 Meeting #84bis R4-1711705
Dubrovnik, Croatia, 21st – 13th October 2017

## Slide 2: Control channel configuration for NR RLM
For each (IS,OOS) BLER pair, at least one set of control channel configuration parameters will be captured for SS block based RLM in 38.133
  The parameter values may be different for IS and OOS
  The parameter values may be different for different numerologies
The parameter values may be different for different BLER pairs, e.g., a smaller DCI and a smaller bandwidth may be used for VoIP compared to eMBB
  The parameter values for (IS,OOS) BLER pair(s) other than (2%,10%) are to be discussed once the other BLER pairs are known

## Slide 3: Control channel configuration parameters
For the BLER pair (2%,10%), the following set of control channel configuration parameters is to be further analyzed until RAN4#85:
  Subcarrier spacing
  Bandwidth
  DCI size
  Aggregation lelvel
  Number of control channel symbols
  Ratio of control channel energy to the SSS RE energy
  Frequency allocation (e.g., contiguous or non-contiguous, frequency location with respect to SS block fequency resources)
Other parameters may also be added, if justified and agreed
In RAN4#85, RAN4 will agree on at least one set of parameters to be captured in 38.133

## Slide 4: Example1: control channel configuration for (2%,10%) BLER pair for 15 kHz
  Bandwidth: 10 MHz and 20 MHz
  DCI size:
    In-sync: 20 bits or 30 bits
    Out-of-sync: 60 bits
  Aggregation lelvel:
    In-sync: 4 and 8
    Out-of-sync: 8
  Number of control channel symbols:
    2 symbols (10 MHz and 20 MHz)
  Ratio of control channel energy to the SSS RE energy: 0 dB
  Frequency allocation: TBD
  NOTE: Other parameters may be added if needed

## Slide 5: Example2: control channel configuration for (2%,10%) BLER pair for 120 kHz
  Bandwidth: 100 MHz and 200 MHz
  DCI size:
    In-sync: 20 bits or 30 bits
    Out-of-sync: 60 bits
  Aggregation lelvel:
    In-sync: 4 and 8
    Out-of-sync: 8
  Number of control channel symbols:
    2 symbols (100 MHz)
    1 symbol (200 MHz)
  Ratio of control channel energy to the SSS RE energy: 0 dB
  Frequency allocation: TBD
  NOTE: Other parameters may be added if needed

## Slide 6: SS block configuration for NR RLM
In RAN4#85, RAN4 will decide whether the same RLM requirements apply for any SS block configurations (e.g., subcarrier spacing, periodicity, etc.)
  The agreement will be reflected in 38.133