## Slide 1: Further optimization of single Tx switched UL
NTT DOCOMO, INC.
3GPP TSG-RAN WG4#85 Meeting
Reno, Nevada, USA, Nov. 27 - Dec 1, 2017
R4-1713183
Agenda item: 9.4.2
Document for: Approval

## Slide 2: Background 1
  RAN4#84bis approved a WF of R4-1711551. Based on one of the agreements in R4-1711551, RAN4 is going to discuss the definition of UL and DL channels from the following options.
  Alt.1. spectrum holdings of a operator in a band
  Alt.2. aggregated UE channel bandwidth configured by the network
  Alt.3. transmission bandwidth
  One of the intensive discussion on this topic was as follows.
    In some cases the amount of MSD is so significant such as 30dB, hence there is no motivation to satisfy it since it is meaningless. Also, there is less motivation to make UEs have less MSD since network will equally handle UEs with large MSD and small MSD even for the same band combination.
    While some said that even with such MSD, the MSD is not always such maximum value according to distance between UE and base stations.

## Slide 3: Background 2
  Even single Tx switched UL is introduced, still UEs are allowed to implement simultaneous uplink transmission feature for difficult band combinations.
  Then, we still have remaining issues to make maximum use of UEs with different MSD values in real network since MSD like 30 dB is the minimum requirement and the UEs would have different level of MSD even for the same band combinations.
  Thus, in this material, we discuss to make good use of UEs with different MSD in real network and how to motivate vendors to implement simultaneous uplink transmission by showing solution to make better performance UEs (with less MSD) to be fully utilized in real network.

## Slide 4: Proposal
UE capability is introduced to indicate that UE supports simultaneous UL with various MSD requirements
  Above UE capabilities are per band combination basis
  Example of MSD requirements is shown in below table. Note that conditions/MSD values in the table are just example, and specific conditions/values will be investigated after December 2017
  The maximum MSD value like 30 dB in the table is defined based on study, while the other MSD values can be determined even without study.
  More specifically, satisfying MSD of 30 dB is mandatory when a UE says that is capable of simultaneous uplink transmission, while MSDs of 20, 10 and 0 dB are optional for UEs with a simultaneous uplink transmission feature.
  Network can optimize their scheduler based on UE capability.
Send LS to RAN2 to inform RAN4 agreements
E-UTRA Band / NRBand/ Channel bandwidth / NRB / Duplex mode |  |  |  |  |  |  |  | Source of IMD | UE capability bit map
LTE-NR DC Configuration | band | UL Fc (MHz) | UL/DL BW (MHz) | UL CLRB | DL Fc (MHz) | MSD (dB) | Duplex mode |  | 
DC_3A-n78A | 3 | 1740 | 5 | 25 | 1835 | 30 | FDD | IMD2 | ’00’
 | n78 | 3575 | 5 | 25 | 3575 | N/A | TDD | N/A | 
DC_3A-n78A | 3 | 1740 | 5 | 25 | 1835 | 20 | FDD | IMD2 | ‘01’
 | n78 | 3575 | 5 | 25 | 3575 | N/A | TDD | N/A | 
DC_3A-n78A | 3 | 1740 | 5 | 25 | 1835 | 10 | FDD | IMD2 | ’10’
 | n78 | 3575 | 5 | 25 | 3575 | N/A | TDD | N/A | 
DC_3A-n78A | 3 | 1740 | 5 | 25 | 1835 | 0 | FDD | IMD2 | ‘11’
 | n78 | 3575 | 5 | 25 | 3575 | N/A | TDD | N/A |