## Slide 1: Way forward on eFeMTC RRM requirements under CRS muting
Ericsson, Nokia, Nokia Shanghai Bell, Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting #85 R4-1713854
Reno, Nevada, US, 27 November – 1 December, 2017
Agenda Item: 8.21.4.2

## Slide 2: Background
Release 15 MTC WI includes the following objective:
  Introduce capability signaling for support for CRS muting outside BL UE narrowband/wideband [RAN1 lead, RAN2, RAN4]
    Enable BL UE to optionally indicate that it does not rely on CRS outside its narrowband/wideband +/- X PRBs, where X is determined by RAN1 and RAN4.
Based on this objective, RAN4 has discussed RRM requirements and made some progress. In this way forward, we capture the agreements on remaining open issues on RRM requirements.

## Slide 3: Proposals on CRS muting
Initial cell acquisition
  Pre-provisioning of EARFCN isCRS transmissions are switched ON over full BW in 1 DL subframe
    Option 1: every 20 ms
    Option 2: every 10 ms
  RAN4 found it beneficial for eMTC UE to have pre-provisioning of EARFCN for eMTC cell to facilitate initial cell search
    beneficial irrespective of CRS muting but benefit is bigger when CRS is muted in the cell
Warm up period
  Warm up period for UEs in CEModeB is defined as 1 DL subframe.

## Slide 4: Proposals on CRS muting
CRS transmission BW for Cat-M2 in the center frequency
  Option 1:
    CRS transmission BW in the center frequency and corresponding UE timing requirements are defined as follows:
  Option 2:
    6 RB for eMTC cell that supports only CEModeA UE
    24 RB for eMTC cell that supports both CEModeA and CEModeB UE
  Option 3:
    12 RB
  Other options are not precluded.
CRS transmission BW in the center frequency | CRS transmissions BW within UE BW in warm-up subframes [RB] | UE Doppler frequency (V) | Timing error (Te_)
6 RBs | 24 | V < 220 Hz | 24*Ts
24 RBs | 24 | V ≥ 220 Hz | 12*Ts

## Slide 5: Network signaling for CRS muting
FFS whether eNB should indicate CRS muting and its associated location and timing information in cell-specific broadcast signaling
  Rel-15 UE can optimize receiver/transmit algorithm depending on whether CRS muting is enabled in the eMTC cell or not

## Slide 6: Proposals
Measurements under high velocity
  Intra-frequency RSRP/RSRQ measurement (measurement period and measurement accuracy) and cell identification requirements under non-DRX for gap pattern ID#0 are reused under high velocity (up to 220 Hz Doppler spread).
  RAN4 shall study the corresponding requirements under DRX for next meeting (RAN4#86).
  UEs under high-velocity shall identify and measure cells on both serving and non-serving carriers
    FFS optimization of gap sharing allocation for high velocity UE
Information about high velocity operation
  FFS whether it beneficial to inform UEs about high velocity operation in a cell.

## Slide 7: Proposals on positioning
RSTD measurements
  When CRS muting is used with eFeMTC, CRS shall not be muted in PRS subframes within the UE bandwidth in the measured cell and the existing FeMTC RSTD requirements shall apply.
UE Rx-Tx measurements for E-CID
  For UE Rx-Tx time difference measurements, the existing requirements provided CRS are available within the UE bandwidth in the serving cell during the UE Rx-Tx measurement period.
RSRP and RSRQ measurements for E-CID
  For RSRP and RSRQ measurements for E-CID, the same principles with respect to CRS muting apply as for general RRM measurements in RRC_CONNECTED.
Transmit timing retuing during UL transmission gap
  CRS transmission shall be assumed over center 6 PRBs during the UL gap for category M1
  CRS transmission shall be assumed over center 24 PRBs during the UL gap for category M2