## Slide 1: WF on WF on RRC Re-establishment and Connection Release with Redirection
Ericsson
3GPP TSG-RAN WG4 Meeting # 86
Athens, Greece, Feb. 26-March 02, 2018
R4-1802774

## Slide 2: Agreements on RRC Connection Release with Redirection Requirements in TS 36.133
Proposal 1: The requirements for RRC connection release with Redirection shall be specified for the following scenarios:
  redirection to NR carrier,
  redirection to UTRA FDD carrier,
  redirection to UTRA FDD carrier
Proposal 2: The requirements for RRC connection release with Redirection to NR carrier shall be specified for the NR target cell’s side conditions comparable to those for performing inter-frequency non-blind handover.
Proposal 3: The requirements for RRC connection release with Redirection to E-UTRA FDD or TDD carrier shall be specified for E-UTRA FDD or TDD target cell’s side condition corresponding to SCH Ês/Iot  -3 dB

## Slide 3: Agreements on RRC Connection Re-establishment Requirements in TS 36.133
Proposal 1: The requirements for RRC connection re-establishment shall be specified for the NR target cell’s side conditions comparable to those for performing NR intra-frequency measurements.
Proposal 2: The time to identify (Tsearch) a target NR cell in the requirements for RRC connection re-establishment consists of time to acquire physical cell ID (PCI) of the target cell i.e. NPSS/NSSS acquisition time.
Proposal 3: The requirements for RRC connection re-establishment shall be specified for the cases when target NR cell is: known and unknown.