## Slide 1: WF on FR2 DL 256QAM
NTT DOCOMO, INC., Nokia, Huawei Deutsche Telekom, BT plc, AT&T, KDDI, Orange, T-Mobile, KT, CMCC, Verizon, Vodafone, China Telecom, Etisalat, SK telecom…]
R4-1807572
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21 - 25 May, 2018
Agenda 7.1.1

## Slide 2: Background
Companies | Detailed proposals
Intel (R4-1806296) | Do not introduce 256QAM DL/UL performance requirements for FR2 in Rel-15.
CATT(R4-1806715) | RAN4 focus up to 64QAM modulation scheme for FR2 in Rel-15 and consider 256QAM in later releases.
Ericsson, Intel, CATT, Samsung, MediaTek, Sony (R4-1807448) | Evaluation of 256QAM should be considered for release 16 No requirements for 256QAM in FR2 are defined in release 15
China Telecom (R4-1806823) | Define DL 256QAM for FR2 as an optional feature in Rel-15. Set new WID for DL 256QAM for FR2 to work on the total requirements for BS and UE.
Huawei (R4-1807520) | Define the DL 256QAM for FR2 as an optional feature in Rel-15. The EVM requirement in Table 2-2 is (3.5% for 256QAM) specified for FR2 BS.
NTT DoCoMo (R4-1807573) | In Rel-15, introduce 256QAM BS Tx EVM requirement in core spec 38.104. Required 256QAM EVM value for NR FR2 BS is [3.5]%.
Nokia (R4-1807874) | Include 256QAM in NR Rel-15 FR2 specification as a manufacturer’s declaration based requirement and reuse FR1 DL Tx EVM requirements.
In RAN4 #87, DL 256 QAM is discussed in following contributions.
In this contribution, the agreements are summarized.

## Slide 3: Agreement
Define DL 256QAM for FR2 as an optional feature in Rel-15.
Only specify 256QAM BS Tx EVM requirement for FR2 in core spec 38.104 in Rel-15, and the required EVM value is 3.5%.
  Considering concerns about power back off and cell coverage issues, the requirement is introduced for Medium Range and Local Area BS.
    FFS for Wide Area BS
  Considering concerns about EVM balancing between BS and UE requirements, the value 3.5% may be reconsidered/revisited in later Release based on the detail analysis in RAN4 if needed.
Not define UE Rx requirements (RF and/or perf) for FR2 256QAM in Rel-15.
  FFS how to introduce 256QAM related UE Rx requirements (RF and/or perf) in later release.
A potential new WID for DL 256QAM for FR2 to complete remaining requirements for BS and UE in Rel-16 can be discussed in RAN plenary. It is up to RAN plenary to approve the new WID.