## Slide 1: Way forward on BS demodulation requirements for eFeMTC
Ericsson
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea (Republic of), 21 – 25 May, 2018
R4-1807976

## Slide 2: Way forward
RAN4 will introduce new PUSCH demodulation requirements with subPRB transmission
  RAN4 will specify the demodulation requirements with 2 of 3 sub-carriers pi/2 BPSK
    FFS: CEModeA and/or CEModeB
  FFS: 3/6 subcarriers with QPSK demodulation requirements
  RAN4 will wait for RAN1 conclusion on the detailed specification
RAN4 will introduce new PUSCH demodulation requirements for CEModeA with the following condition. Interested companies are encouraged provide the simulation results for alignment
  8 PUSCH repetitions
  FRC A3-2 (QPSK 1/3, TBS=600bit, 6PRB)
  Bandwidth 3, 5, 10, 15, and 20MHz
  ETU200
  Antenna configuration: 1x2