## Slide 1: Way Forward on Concluding the NR Test Methods SI
Intel, CATR, Rohde & Schwarz, Anritsu, Spirent
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21th – 25th May, 2018
Agenda item: 7.13
R4-1808541

## Slide 2: RRM Testing Methodology
Ad-hoc agreements
  Far field criteria:
    Far field testing is used as baseline for RRM testing. Other conditions can be discussed. When far field testing is used for RRM, Far Field criteria and applicability defined for the DFF UE RF test method applies
  Do not preclude using demodulation baseline setup to perform selected RRM metrics testing. Requirement applicability should be investigated in the NR WI during simulation and requirement definition work
  Do not preclude using near field to perform selected RRM metrics testing. Requirement applicability in near and far field should be investigated in the NR WI during simulation and requirement definition work
    Note: Near field corresponds to the measurement distance smaller than the distance for the Far field
  TDL channel methodology for RRM uses the framework of Demod, while the channel parametrization for RRM testing will be defined in the NR WI during simulation and requirement definition work
  Quiet zone
    A DFF measurement setup has the center of the QZ zone located at the center of the rotational axes (of DUT and measurement antenna). For the multi-probe RRM measurement baseline setup based on DFF, the vertices of the N probes have to be aligned to the resulting center of the QZ. The center of the QZ is taken as the reference for MU definition for each probe. The same QZ size as per RF measurement baseline setup based on DFF applies

## Slide 3: RRM Testing Methodology
Ad-hoc agreements
Test metrics and initial MU assessment
  Test parameters for RRM testing to be controlled by TE
    SNR of DL signal at reference point
    DL power level at reference point (e.g. EPRE) (from AoA)
    Relative DL power level of 2 signals at reference point
      From intra-frequency or inter-frequency cells
      From the same AoA or different AoAs
    Relative DL timing of 2 signals at reference point
    Faded DL channel for each signal
    AoA for signals arriving at reference point
  Metrics for RRM testing
    UL PRACH level transmitted by the UE
    Relative UL PRACH level transmitted by the UE
    Timing of UE UL transmission relative to DL signal
    Relative timing change of UE UL transmission relative to DL signal
    Timing measurement of UL events caused by events on the DL
  Open issues for RRM test parameters and metrics initial MU assessment
    Reference point definition for Test parameters for RRM testing to be controlled by TE is FFS (e.g. SNR)
    Feasibility of implementation of identified test parameters and metrics
    Initial assessment of the MU elements related to the identified metrics and parameters
      Reuse the MU elements in DFF method for RF testing as starting point, define the new contributors related to RRM metrics (if any)
      Identify key elements contributing to the MU.
      At least analyse the MU factors and provide initial assessment for DL SNR and power level accuracy/range
      Detailed analysis of MU is up to RAN5

## Slide 4: UE Demodulation Testing Methodology
Ad-hoc Agreements
  Allow the operation of the UE Demodulation test system in the radiative near field
  Minimum measurement distance defined according to the following formula:
    where:
      D = DUT radiating aperture (D is vendor declared)
      λ = wavelength

## Slide 5: UE Demodulation Testing Methodology
Proposals
  Key test parameters for UE demodulation testing to be controlled by TE
    SNR of DL signal at reference point
      Reference point definition for DL SNR is the [UE RX baseband port]
    Faded DL channel
  Metrics for UE demodulation testing
    Typical UE Demodulation and CSI metrics (e.g. throughput, block-error rate, CSI statistics) similar to the metrics defined in the TS 36.101.
  Remaining open issues
    Applicability for demod measurement set-up to be refined for possible far field and near field solutions.
    Identification of MU factors contributing to DL SNR accuracy and range
    Achievable SNR accuracy and SNR range
      Initial assessment of SNR accuracy and SNR range completed.
      Conclusions on the SNR accuracy and SNR range are FFS
    Note: Detailed analysis of MU for SNR is up to RAN5

## Slide 6: Channel Models
Ad-hoc agreements
  Measurement system shall support emulation of static propagation conditions for RRM and UE Demodulation/CSI tests
  Details of static channels definition and how it is emulated in chamber can be further discussed
    Static channel model definition
      Option 1: Static channel models as defined in TS 36.101 Annex B.1.1
      Option 2: Static channel models is the model invariant in time
  Make decision on Reduction of the number of modeled taps for TDL as a part of NR WI performance part
  Use equidistant delay modelling grid for TDL channel models after DS scaling with grid step ΔT ≤ 1/BW.
    BW value
      Single carrier scenarios: BW = [200] MHz
      Intra-band CA scenarios: Decision on BW value will be made in the NR WI performance part.
    Paths that end up with the same delay will be combined into a single path by adding their respective powers
  Option 1 methodology is feasible from test equipment perspective
  Clarifications on Option 2 channel modeling methodology
    Step 1 and 2: Follow the procedure from 38.901 to convert a CDL into a TDL channel model
      Note: Step 1 and 2 refer to Option 2 steps in R4-1805895

## Slide 7: Channel Models
Proposals
  Static channel models definition is FFS
  Option 2 multi-path fading channel methodology
    Option 2 methodology allows non-Jakes Doppler fading modeling.
    Option A: Multi-path fading propagation conditions between the gNB emulator and test chamber probe is modelled as Tapped Delay Line (TDL) which is derived based on Clustered Delay Line (CDL).
      Detailed methodology is described in TP R4-1808518
      Methodology is feasible from test equipment perspective
    Other TDL modeling options based on alternative approaches for Doppler fading modeling are not precluded (e.g. sum of sinusoids, noise filtering)