## Slide 1: WF for NR PRACH demodulation
Ericsson, […]
R4-1813757
Document for: Approval
3GPP TSG-RAN WG4 RAN#88bis
Chengdu, China, 8 – 12 October, 2018
Agenda: 7.13.2.4

## Slide 2: Background
The following WFs were approved:
  R4-1811728, WF on NR PRACH demodulation requirements, RAN4#88

## Slide 3: Preamble format
Set requirements for Preamble:
  Short sequence
    Format A1, A2, A3, B4, C0 and C2
  Long sequence:
    Format 0
SCS: cover 15kHz, 30kHz, 60kHz (FR2) and 120kHz for short sequence
For each preamble/SCS, set requirements for:
  AWGN channel and 0 kHz offset
  TDL channel and frequency offset specified in “Timing Offset” slide.

## Slide 4: Timing Offset
Reuse LTE timing offset sequence for format 0
  Timing offset start value:
    50% of Ncs
  Increased within the loop, adding 0.1us in each step (up to 0.9us)
  Then loop is reset and restart again.
Timing offset shall be scaled according to SCS and format
  To be further investigated, Email discussion. Deadline: Oct 26th
Tolerance on timing offset error should be further investigated for next meeting.
  Option1: Scaling according to SCS
  Other option is not precluded
  Email discussion. Deadline: Oct 26th

## Slide 5: Frequency offset
FR1
  400 Hz
FR2
  4000 Hz

## Slide 6: Logical sequence index
Short sequence:
  0
Long sequence:
  22

## Slide 7: Ncs and v values
Ncs:
  15 kHz:
    23
  30 kHz
    46
  60 – 120 kHz:
    69
v value
  Format 0: 32
  Short sequence : 0

## Slide 8: Simulations assumptions for 1T2R, 1T4R, and 1T8R