## Slide 1: Summary of enhanced MIB/SIB1 reading simulation results
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #88bis R4-1813990
Chengdu, P.R of China, 8 – 13 October 2018
Agenda Item: 6.5.4

## Slide 2: Simulation assumptions
Parameters | Values
Serving cell SCH Es/Iot | -6dB
Target cell SCH Es/Iot | -15dB
UE receive antennas | 1
BS transmit antennas | 2
Fading channel | ETU1, EPA1
PBCH repetition | Configured as specified in TS36.211 6.6.4
SIB1-BR repetition level | 16 (schedulingInfoSIB1-BR = 3)
TBS for SIB1-BR | 208 bits (schedulingInfoSIB1-BR = 3)
MIB assumption | The network does not change the MIB payload information across MIB TTI (40ms) except for the system frame number (SFN)
SIB1-BR assumption | The network does not change the SIB1-BR information across SIB1-BR TTI (80ms).
Agreed simulation assumptions in R4-1805954:

## Slide 3: Simulation results of SI reading in CEModeB using cross TTI accumulation
Note: the delays in the table above are excluding the implementation margins.
SI type | Ericsson | Huawei | Qualcomm
MIB (target success rate) | 480 ms (95%) | [120ms] ( 90%) | 1500 ms (95%)
SIB1-BR (target success rate) | 1440 ms (95%) | [1600ms] ( 90%) | 1280 ms (95%)
Reference | R4-1804631 | R4-1804730 | R4-1806851