## Slide 1: Way Forward on RF exposure compliance in FR2
Intel Corporation, Nokia, LGE
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8 – 12 October 2018 Agenda Item: 7.6.7.1.2
R4-1814176

## Slide 2: Background
Under certain conditions, the amount of power back-off needed for regulatory compliance of FR2 devices will have an impact on performance and may lead to radio link failure [1,2]
From network and system perspective, this sudden, drastic and even unpredictable reduction of NR UL power or even drop of NR UL transmission is problematic as the network does not know why this sudden NR UL power drop or complete NR UL transmission drop has happened
Some actions could help prevent link failure from the UE and system
Standards and regulations are under discussion

## Slide 3: Way Forward
RAN4 should decide whether to solely rely on P-MPR to maintain compliance with RFE limits, or introduce necessary mitigation techniques to prevent the radio link failure and optimize performance
  Possible options
    Introduce a maximum uplink duty cycle restriction as optional
    UE provides information for the network to avoid UL link failure due to large power back-off
    Other techniques are not precluded, for example:
      Dynamic uplink duty cycle restriction
      Beam refinement requests

## Slide 4: References
[1] R4-1804127, “Performance considerations for RF exposure compliance in FR2,” Intel Corporation, RAN4 #86-Bis, April 2018
[2] R4-1813169, “FR2 UE RF exposure compliance and new UE P-MPR information to network,” Nokia, Nokia Shanghai Bell, RAN4 #88-Bis, October 2018
[3] R4-1813526, “Uplink duty cycle and power back-off considerations for FR2,” Intel Corporation, RAN4 #88-Bis, October 2018