## Slide 1: Way forward on R16 NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #90
Athens, Greece, 25 Feb – 1 Mar, 2019
R4-1902031
Document for: Approval

## Slide 2: Background: objectives in new WID: NR mobility enhancements (RP-181433)
To study solution(s) to reduce interruption time during HO/SCG change focusing on the following identified solutions but not limited.
  Handover/SCG change with simultaneous connectivity with source cell and target cell.
  Make-before-break
  RACH-less handover
To study solution(s) to improve HO/SCG change reliability and robustness especially considering challenges in high/med frequency focusing on the following identified solutions but not limited.
  Conditional handover
  Fast handover failure recovery
RAN2 should avoid increasing signalling overhead.
Note: LTE mobility enhancements should be used for baseline for fast handover failure recovery, Make-before-break and RACH-less handover.
To specify the solutions and agreements agreed during the above study phase. [RAN2/RAN1/RAN3/RAN4]
Note: The following aspects should be considered in above objectives.
- Inter and intra frequency handover/SCG change
- Inter-CU, intra-CU/inter-DU and intra-DU handover/SCG change
- Synchronous and asynchronous deployments as assumed in Rel-15 NR
- UE capability on the number of Tx/Rx chains
- Low and high velocity
- FR1 and FR2 frequencies

## Slide 3: Agreements on Handover/SCG change with simultaneous connectivity with source cell and target cell
RAN4 to study the feasibility of simultaneous connectivity to both serving and target NR cells in different scenarios.
  the RAN4 response in LS (R4-1902030) in R16 LTE FeMobility WI can be used as starting point.
  On top of response in LS (R4-1902030) at least the following additional aspects shall be considered:
    Same or different SCS between the source and target cells.
    Handover involving cell(s) in FR2, where Tx/Rx beamforming is used.

## Slide 4: Agreements on make-before-break handover
RAN4 confirms the feasibility of make-before-break handover in at least FR1 intra-frequency synchronous deployment when source and target cells have the same BW and SCS.
Feasibility (and corresponding conditions if feasible) of make-before-break handover in other scenarios will be further studied if requested by RAN2 according to RAN2 progress.

## Slide 5: Agreements on RACH-less handover
RAN4 confirms the feasibility of RACH-less handover in FR1 for at least
  intra-frequency synchronous case with same BW and SCS between source and target cells
  same TA or zero TA between source and target cells.
  Single and multiple BS Tx beam deployment
Feasibility (and corresponding conditions if feasible) of RACH-less handover in other scenarios will be further studied if requested by RAN2 according to RAN2 progress.