## Slide 1: WF for R16 LTE-MTC/NB-IoT coexistence with NR
Ericsson, Nokia, ZTE, Dish, CHTTL
3GPP TSG-RAN4 Meeting #90
Athens, Greece, 25 Feb- 1 March 2019
R4-1902681

## Slide 2: Background
RAN4 has sent LS [1] to RAN on the scope of NR and NB-IoT/eMTC coexistence studies.
In RP-182891, “Revised WID: Additional MTC enhancements for LTE” one of the objectives of improvements for machine-type communications for BL/CE UEs is as below:
  Coexistence with NR:
    Study NR and LTE specifications to identify possible issues related to coexistence of LTE-MTC with NR [RAN4, RAN1, RAN2]
In RP-182902, “WID revision: Additional enhancements for NB-IoT” one of the objectives of improvements for machine-type communications for NB-IoT UEs is as below:
  Coexistence with NR
    Study NR and LTE specifications to identify possible issues related to coexistence of FDD/TDD NB-IoT with NR [RAN4, RAN1, RAN2]
The RAN4 work for these WIs started at RAN4#90, and the coexistence objective is treated in contributions [2] – [6] for LTE-M and [7] – [10] for NB-IoT.

## Slide 3: WF on scope of the R16 co-exsiting study - LTE-M
Coexistence between R15 NR and R13/R14/R15 LTE-M:
  For eMTC in-band operation co-existence with NR, including the case of NR configured in 15kHz SS Block SCS and the case of 30kHz SS Block SCS as specified in 38.101-1, investigate the following [1]:
    15KHz, 30KHz, and 60KHz numerologies for NR FR1 concerned bands, with higher priority given first to 15kHz and then to 30kHz
    Study feasible eMTC placement allocation without RF backward compatibility impact and compatible with Rel’13 eMTC and Rel’15 NR, to operate simultaneously within various NR channel bandwidths
    Channel raster, PRB and subcarrier grid alignment between eMTC and NR
    synchronization issue between eMTC and NR, including timing advance
  With the following additions from [4][6]:
    Frequency band support in LTE and NR
    Testablity applicance on RF, FFS on RRM and demod
    Backward compatiblty on R15 NR, R13/R14/R15 LTE-M
Coexistence between R15/R16 NR and R16 LTE-M:
  Based on R16 LTE-MTC WI and scope to be decided on next meeting
Time plan
  Co-existing work for R15 start firstly
  Co-exsting work for R16 start secondly after RAN1 R16 co-existing enhance feature finalized

## Slide 4: WF on scope of the R16 co-exsiting study - NB-IoT
Coexistence between R15 NR and R13/R14/R15 NB-IoT:
  NB-IoT standalone coexistence with NR is already addressed with MSR specification (TS 37.104).
  For NB-IoT in-band and guard band operation co-existence with NR investigate the following:
    15KHz, 30KHz, and 60KHz numerologies for NR FR1 concerned bands, with higher priority given first to 15kHz and then to 30kHz
    Channel raster, PRB and subcarrier grid alignment between NB-IoT and NR
    Study feasible NB-IoT carrier(s) placement allocation without RF backward compatibility impact and compatible with Rel’13 NB-IoT and Rel’15 NR, to operate simultaneously within various NR channel bandwidths
    Study if the +6dB downlink RE power boosting can still be allowed for both in-band and guard band operation modes when co-existing with NR
    Synchronization issue between NR and NB-IoT, including timing advance
  With the following additions from [9][10]:
    Frequency band support in NB-IoT and NR
    Testablity applicance on RF, FFS on RRM and demod
    Backward compatiblty on R15 NR, R13/R14/R15 NB-IoT
Coexistence between R15/R16 NR and R16 NB-IoT:
  Based on R16 NB-IoT WI and scope to be decided on next meeting
Time plan
  Co-existing work for R15 start firstly
  Co-exsting work for R16 start secondly after RAN1 R16 co-existing enhance feature finalized

## Slide 5: References (LTE-M)
[1] R4-1811841,LS to RAN on the scope of NR and NB-IoT/eMTC Coexistance, Huawei
[2] R4-1900505, Discussion on NR and MTC coexistence, ZTE Corporation
[3] R4-1901656, overview of LTE-M and NR co-existing,Ericsson
[4] R4-1901657, scope of LTE-M and NR co-existing, Ericsson
[5] R4-1901658, channel raster of LTE-M and NR co-existing,Ericsson
[6] R4-1901971, Recommendations on LTE-MTC coexistence with NR Nokia, Nokia Shanghai Bell

## Slide 6: References (NB-IoT)
[7] R4-1900507, Discussion on NR and NB-IoT coexistence, ZTE Corporation
[8] R4-1901400,NB-IoT NR coexistence - Channel raster,Ericsson
[9]R4-1901401, NB-IoT and NR coexistence scope,Ericsson
[10] R4-1901487,Recommendations on NB-IoT coexistence with NR , Nokia, Nokia Shanghai Bell