## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’An, China, 8th – 12th April 2019
Huawei, HiSilicon
Way forward on RRM requirements for simultaneous SSB and CSI-RS
R4-1904711

## Slide 2: Background
UE behavior in receiving SSB/CSI-RS or CSI-RS/CSI-RS for RLM/BFD/CBD/L1-RSRP measurements in the same OFDM symbol has been discussed in RAN4.
For FR2, the Rx beam sweeping aspect is discussed based on RAN1 LS R1-1809890, and reply LS is in R4-1904684.
Following are agreements from online session.
  The concurrent reception of signal in group 1 and group 2 can be done as long as the UE can use the same Rx beam for reception (or Rx beam sweeping is not needed) and the SCS is same (unless UE can support simultaneousRxDataSSB-DiffNumerology).
  If the RS in group 2 is QCL-Type D with RS in group 1 and the QCL association is known to UE, UE can receive both RS in group 1 and group 2 in the same OFDM symbol when UE is not expected to sweep its Rx beam in FR2
    The agreement is not applicable to CSI-RS base L3 measurement in Rel-15.
  The UE is not required to receive CSI-RS in the PRBs that overlap with an SSB.

## Slide 3: WF on FR1 UE requirements
For FR1, if RS1 for RLM/BFD/CBD/L1-RSRP measurement is in the same OFDM symbol as RS2 for RLM/BFD/CBD/L1-RSRP measurement,
  if the SCS of RS1 and RS2 are different and UE does not support simultaneousRxDataSSB-DiffNumerology, UE is not required to measure either RS1 or RS2, and longer evaluation or measurement period for RLM/BFD/CBD/L1-RSRP would be expected.
  Otherwise, UE is required to measure both RS1 and RS2 and the existing requirements for RLM/BFD/CBD/L1-RSRP apply
  Note: only SSB and CSI-RS may have different SCS
  No requirement will be defined for the longer evaluation or measurement period in Rel-15

## Slide 4: WF on FR2 UE requirements
For FR2, if RS1 for RLM/BFD/CBD/L1-RSRP measurement is in the same OFDM symbol as RS2 for RLM/BFD/CBD/L1-RSRP measurement,
  In the following conditions UE is not required to measure either RS1 or RS2, and longer evaluation or measurement period for RLM/BFD/CBD/L1-RSRP would be expected.
    if RS1 and/or RS2 is SSB or
    if RS1 and/or RS2 is CSI-RS resource in a resource set configured with repetition ON or
    if RS1 and/or RS2 is configured in q1 when beam failure is detected, or
    if RS1 and RS2 is not QCL-ed w.r.t. QCL-TypeD, or the QCL information is not known to UE, or
    if the SCS of RS1 and RS2 are different and UE does not support simultaneousRxDataSSB-DiffNumerology
    Note: only SSB and CSI-RS may have different SCS
    No requirement will be defined for the longer evaluation or measurement period in Rel-15
  Otherwise, UE is required to measure both RS1 and RS2 and the existing requirements for RLM/BFD/CBD/L1-RSRP apply

## Slide 5: WF
In Rel-16 the UE requirements in measuring more than one RS for RLM/BFD/CBD/L1-RSRP measurement in the same OFDM symbol can be revisited.