## Slide 1: WF on RF parameters for NR V2X UE
LG Electronics
3GPP TSG-RAN WG4 #90BIS Meeting
Xian, China, 08th – 12th April, 2019
Agenda Item: 8.4.1
Document for : Approval
R4-1905238

## Slide 2: Background (1)
AGC setting time [1][2][3][4][5][6][7]
  In previous RAN4 meeting, RAN4 agreed to provide simulation results according two options
    AGC settling time
      FFS if same or different AGC settling time shall be applied for different SCS
      AGC settling time will be derived under assumption of minimum V2X resource allocation RB size restrictions. RBs size restrictions are FFS:
        Option1
          At least 10RBs for 15kHz
          At least 5 RBs for 30kHz
          At least 3 RBs for 60kHz
        Option2
          At least 10RBs for all SCSs
Enhanced IBE model [5][8][9][10]
  RAN4 will further discuss on the enhanced IBE model for NR V2X UE.
  Interested companies are encouraged to provide the preferred IBE model for NR V2X UE at next RAN4 meeting.
  Based on the analyzed results, RAN4 can send LS to inform the IBE model at FR1.

## Slide 3: Background (2)
Time/Freq. Error [1][11]
  RAN4 will further discuss on the TBD RF parameters in Response LS (R4-1816666)
  Timing error
    FR1/FR2
      gNB based TE : reuse NR UE UL transmission timing error defined in Table 7.1.2-1 in TS38.133
      GNSS based TE : FFS
      NR UE sync. TE: FFS
  Frequency error
    FR1/FR2
      gNB synchronization reference source: ±0.1 ppm for gNB synchronization reference source
      GNSS synchronization reference source: FFS
      NR UE synchronization reference source: FFS

## Slide 4: AGC settling time
Alternative 1
  R4-1903029, "Reply LS on UE RF parameters for NR V2X service," LG Electronics France
    AGC settling time
      AGC time :  35us for all SCS for option1 [12]
      AGC time :  35us for 15kHz for opton2 [12]
       18us or/and 35us for 30kHz
       9us or/and 3618us for 60kHz
  Supporting companies: LGE, MTK, HW, CMCC, Spreadtrum
  AGC settling time proposal from interested vendors will be referred in LS
AGC time | LGE | Intel | MTK | QC | Ericsson | HW
Option1 | 36 us for all SCS | 36us for all SCS | - |  | Similar LTE (1 symbol) | 
Option2 | 0.5 OFDM symbol |  | 27us for 15kHz, 14us for 30kHz, 8us for 60kHz | 35 us for all SCS |  | 
Note |  | Option1 for max AGC | Only option2 with different AGC time | 35us for all SCS with at least 10RBs | Option1 for same AGC time | Different implementation should be considered

## Slide 5: AGC settling time
Alternative 3
  R4-1903029, "Reply LS on UE RF parameters for NR V2X service," LG Electronics France
    AGC settling time
      AGC time :  35us for all SCS with at least 10RBs
      Reasoning & Justification : realistic scenarios need to be consider when we decide AGC value according to measure RB size
  Supporting companies: Ericsson, Intel, QC, VW, InterDigital
  AGC settling time proposal from interested vendors will be referred in LS
AGC time | LGE | Intel | MTK | QC | Ericsson | HW
Option1 | 36 us for all SCS | 36us for all SCS | - |  | Similar LTE (1 symbol) | 
Option2 | 0.5 OFDM symbol |  | 27us for 15kHz, 14us for 30kHz, 8us for 60kHz | 35 us for all SCS |  | 
Note |  | Option1 for max AGC | Only option2 with different AGC time | 35us for all SCS with at least 10RBs | Option1 for same AGC time | Different implementation should be considered

## Slide 6: WF on AGC
There was no consensus in #90BIS RAN4 meeting between Alt. 1 and Alt.3
  RAN4 further discuss on the AGC settling time.
  Some parameters impact to AGC settling are waveform, RB size, SCS, number of carriers and number of receiver chains. AGC settling reported to RAN1 shall also consider the implementation aspects.
    There is no consensus in RAN4 on the total AGC settling time.

## Slide 7: IBE
NR V2X
  Enhanced IBE
    There are some argument points for the target IBE requirements  No consensus
IBE | Intel | LGE | QC | Ericsson
General | 7dB tightening | Satisfy | No or limited gain for PRR aspect | ΔRB=1 has no margin, tightening of IBE requirement should be start from ( ΔRB=2), 3 dB tightening is recommended
Carrier leakage | 10dB tightening | Satisfy with small margin |  | 
I/Q leakage | Remove and replace general IBE | Satisfy with small margin |  | 
Note | Overall 7dB tightening by Noise floor | Further study on the impact of non-linearity Tx chain | RAN4 can study after RAN1 target design agreement | Option1 for same AGC time

## Slide 8: Draft LS for Time/Freq. error
NR V2X
  R4-1903029, "Reply LS on UE RF parameters for NR V2X service," LG Electronics France
    Timing error
      gNB based TE at FR1 and FR2 : follow specified Timing Error in TS38.133. It is starting point, RAN4 will further analyse the timing error by gNB synchronization source and subject to change during NR V2X WI phase.
      GNSS based TE at FR1 : Time error is 12*64Tc for 15kHz. It is starting point, RAN4 will further analyse the timing error by GNSS synchronization source and subject to change during NR V2X WI phase. Other cases are FFS
      UE sync. TE at FR1 : Time error is 12*64Tc for 15kHz. Other cases are FFS
    Frequency error
      FR1: ±0.1 ppm for gNB/GNSS/NR UE synchronization reference source
      FR2: ±0.1 ppm for gNB/GNSS/NR UE synchronization reference source

## Slide 9: Reference
[1] R4-1903029, "Draft reply LS on NR V2X UE RF parameters for NR V2X service at FR1," LG Electronics
[2] R4-1903096, "AGC settling time for V2X," Qualcomm Inc.
[3] R4-1903177, "Discussion on AGC issue for NR V2X," Huawei, HiSilicon
[4] R4-1903662, "On AGC settling time," MediaTek inc.
[5] R4-1903998, "On AGC settling time and IBE for NR V2X," LG Electronics
[6] R4-1904190, "AGC settling time analysis," Huawei, HiSilicon
[7] R4-1904256, "AGC settling time discussion," Ericsson
[8] R4-1904257, "On IBE requirement discussion," Ericsson
[9] R4-1903118, "On NR V2X in-band emission model," Qualcomm Inc.
[10] R4-1903125, "On NR V2X IBE," Intel Corporation
[11] R4-1902990, "On NR V2X RRM characteristics," Intel Corporation
[12] R4-1902513, “WF on the NR V2X RF parameters and transient period,” LG Electronics