## Slide 1: Way forward on Tx switching between two uplink carriers
3GPP TSG-RAN WG4 Meeting #93
Reno, Nevada, US, Nov 18 - 22, 2019
Agenda: 9.13.1.6
R4-1916084
China Telecom

## Slide 2: WF on switching period and transient period
Transient period
  Define transient period in addition to the switching period
  Length of transient period: 2x10 us for UL CA and SUL, 10 us + 20 us for EN-DC
Length of UL switching period for defining UE RF requirements:
  Non-zero value
    Option A: {35us, 140 us, 250us} or {1, 4, and 7} OFDM symbols for 30kHz SCS
    Option B: {35us, 140 us} or {1, 4} OFDM symbols for 30kHz SCS
    Option C: only 35us
  FFS whether to define 0us switching period

## Slide 3: WF on handling of DL reception interruption
Option A: Define different capabilities for UEs with and without DL reception interruption
  If UE does not report this capability, it means there is no DL reception interruption.
Option B: DL reception interruption is not allowed.
Option C:
  No DL reception interruption for the following duplex mode combinations: (carrier 1 + carrier 2)
    SUL+TDD
    FDD+TDD
    TDD+TDD with synchronous UL-DL configurations the same UL-DL pattern
  Other duplex mode combinations: allowed for one or two DL carriers based on UE capability reporting
Send LS to RAN1 and ask RAN1’s feedback on RAN1 spec impact if there is DL reception interruption in some scenarios.

## Slide 4: WF on UE RF requirements
Type of new RF requirement
  Define requiremnet for switching period and transient period, and verify that UE supports switching period being located on either one of the NR FR1 UL carriers (i.e., for UL CA and SUL)
    Define time mask requirement, and no other RF requirements will be defined. RAN1 feedback will be taken into account when defining UE RF requirements.
For UE supporting UL Tx switching, it is mandated to support 2-layer UL-MIMO transmission and single-layer transmission on carrier 2 following the BS scheduling and rank adaptation (if rank adaptation is applicable).

## Slide 5: WF on power class
Power class declaration will NOT be changed between case 1 and case 2.
Rel-16 power class singling will be followed for Tx switching between case 1 and case 2.

## Slide 6
Thanks!